## Slide 1: Electronics Systems (938II)
Lecture 2.1
Building Blocks of Electronic Systems – MUX, DEMUX, XOR, Comparator

## Slide 2: Building Blocks of Electronic Systems*
An electronic system is made of combinational and/or sequential circuits
  Combinational circuit
    Output depends only on the current input(s)
  Sequential circuit
    Output depends on both the current input(s) and the current state
    Current state = previous output → It has memory

## Slide 3: Building Blocks of Electronic Systems*
Combinational circuits
  The best known and most widely used are the NOT, AND and OR gates
  Any logic function can be implemented using a combination of these gates
  Or, NOT, NOR and NAND gates
    Remember advantages of active-low logic
    Rember De Morgan’s laws

## Slide 4: Building Blocks of Electronic Systems*
Combinational circuits
  Other primitives exist
  For example, the multiplexer (or MUX)

## Slide 5: Multiplexer (or MUX)*
Logic symbol and functionality
  1 (input) control signal = sel
  1 output = y
  N (data) inputs, e.g., N = 2: a, b
  If sel = 0 → y = a, else (sel = 1) → y = b
  Bit width of sel must be
  Output and (data) inputs can also be multi-bit
a
b
y
sel
0
1

## Slide 6: Multiplexer (or MUX)*
Gate-level circuit
  If sel = 0 → y = a, else (sel = 1) → y = b
a
b
y
sel
0
1

## Slide 7: Multiplexer (or MUX)*
Gate-level circuit
  If sel = 0 → y = a, else (sel = 1) → y = b
a
b
y
sel
0
1

## Slide 8: Multiplexer (or MUX)*
Gate-level circuit
  If sel = 0 → y = a, else (sel = 1) → y = b
a
b
y
sel
0
1

## Slide 9: Multiplexer (or MUX)*
Gate-level circuit
  If sel = 0 → y = a, else (sel = 1) → y = b
a
b
y
sel
0
1

## Slide 10: Multiplexer (or MUX)*
Gate-level circuit
  If sel = 0 → y = a, else (sel = 1) → y = b
a
b
y
sel
0
1
(NAND gate-based)

## Slide 11: Multiplexer (or MUX)*
Gate-level circuit
  If sel = 0 → y = a, else (sel = 1) → y = b
a
b
y
sel
0
1
(NAND gate-based)

## Slide 12: Multiplexer (or MUX)*
Gate-level circuit
  If sel = 0 → y = a, else (sel = 1) → y = b
a
b
y
sel
0
1
(NAND gate-based)

## Slide 13: Multiplexer (or MUX)*
Gate-level circuit
  If sel = 0 → y = a, else (sel = 1) → y = b
a
b
y
sel
0
1
(NAND gate-based)

## Slide 14: Multiplexer (or MUX)*
Gate-level circuit
  If sel = 0 → y = a, else (sel = 1) → y = b
a
b
y
sel
0
1
(NAND gate-based)

## Slide 15: Multiplexer (or MUX)*
Gate-level circuit
  If sel = 0 → y = a, else (sel = 1) → y = b
a
b
y
sel
0
1
(NAND gate-based)

## Slide 16: Demultiplexer (or DEMUX)*
Opposite of MUX
Logic symbol and functionality
  1 (input) control signal = sel
  N outputs, e.g., N = 2: a, b
  1 (data) input = i
  If sel = 0 → a = i, else (sel = 1) → b = i
  Bit width of sel must be
  Outputs and (data) input can also be multi-bit
sel
a
b
i
sel
a
b
0
1
i

## Slide 17: XOR (or exclusive-OR)*
Description
  Two inputs
  One output
  Functionality
    One input or the other one is equal to (logic) 1
    Exclusive OR (one or the other)
  Boolean symbol:
Truth table
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 18: XOR (or exclusive-OR)*
Another single-gate logical function
  Logic symbol = gate-level symbol
(gate-level = logic symbol)

## Slide 19: XOR (or exclusive-OR)
Another single-gate logical function
  Logic symbol = gate-level symbol
(gate-level = logic symbol)
(transistor-level)

## Slide 20: XOR (or exclusive-OR)
Let’s verify it works
(transistor-level)
Truth table
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 21: XOR (or exclusive-OR)
Let’s verify it works
(transistor-level)
Truth table
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 22: XOR (or exclusive-OR)
Let’s verify it works
(transistor-level)
Truth table
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 23: XOR (or exclusive-OR)
Let’s verify it works
(transistor-level)
Truth table
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 24: XOR (or exclusive-OR)
Let’s verify it works
(transistor-level)
Truth table
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 25: XNOR (or exclusive-NOR)*
Logical complement of XOR
  Boolean symbol:
  Another single-gate logical function
    Logic symbol = gate-level symbol
(gate-level)
(transistor-level)
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Truth table

## Slide 26: XNOR (or exclusive-NOR)
Logical complement of XOR
  Boolean symbol:
  Another single-gate logical function
    Logic symbol = gate-level symbol
(gate-level)
(transistor-level)
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Truth table

## Slide 27: Comparator*
Looking at the truth table of the XOR (or XNOR) function, essentially it indicates if inputs are different (or equal)
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
XOR truth table
XNOR truth table
1 when inputs are different
1 when inputs are equal

## Slide 28: Comparator*
Looking at the truth table of the XOR (or XNOR) function, essentially it indicates if inputs are different (or equal)
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
XOR truth table
XNOR truth table
1 when inputs are different
1 when inputs are equal
Can be used to build comparators
check if two vectors (single-bit or multi-bit) are different (or equal)

## Slide 29: Comparator*
Parallel version: DIFF = 1, if inputs are different (otherwise 0)
1-bit comparator
4-bit comparator

## Slide 30: Comparator*
Parallel version: DIFF = 1, if inputs are different (otherwise 0)
  Inputs
    a = {a3 a2 a1 a0}
    b = {b3 b2 b1 b0}
  Example
    a = {1101}
    b = {1101}
4-bit comparator

## Slide 31: Comparator*
Parallel version: DIFF = 1, if inputs are different (otherwise 0)
  Inputs
    a = {a3 a2 a1 a0}
    b = {b3 b2 b1 b0}
  Example
    a = {1101}
    b = {1011}
4-bit comparator

## Slide 32: Comparator*
Iterative (or sequential) version: EQ = 1, if inputs are equal
n-bit comparator

## Slide 33: Comparator*
Iterative (or sequential) version: EQ = 1, if inputs are equal
n-bit comparator
CMP

## Slide 34: Comparator*
Iterative (or sequential) version: EQ = 1, if inputs are equal
n-bit comparator
CMP
0 | x | x | x | 0
1 | 0 | 0 | 1 | 1
1 | 0 |  | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1
0 | x | x | x | 0
1 | 0 | 0 | 1 | 1
1 | 0 |  | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1
CMP truth table

## Slide 35: Comparator*
Iterative (or sequential) version: EQ = 1, if inputs are equal
  Example: 4-bit comparator
    a = {1101}
    b = {1101}
0 | x | x | x | 0
1 | 0 | 0 | 1 | 1
1 | 0 |  | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1
0 | x | x | x | 0
1 | 0 | 0 | 1 | 1
1 | 0 |  | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1
CMP truth table

## Slide 36: Comparator*
Iterative (or sequential) version: EQ = 1, if inputs are equal
  Example: 4-bit comparator
    a = {1101}
    b = {1011}
0 | x | x | x | 0
1 | 0 | 0 | 1 | 1
1 | 0 |  | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1
0 | x | x | x | 0
1 | 0 | 0 | 1 | 1
1 | 0 |  | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1
CMP truth table

## Slide 37: Comparator*
Iterative (or sequential) version: EQ = 1, if inputs are equal
  For very long n-bit input vectors (i.e. n is very high), it may reduce resource consumption
  But very long path/delay

## Slide 38: Exercise with SystemVerilog
Implementation of a MUX and simulation with Modelsim

## Slide 39: Exercise with SystemVerilog
Implementation of a MUX and simulation with Modelsim

## Slide 40: Exercise with SystemVerilog*
Implementation of a MUX and simulation with Modelsim
Continuous assignment
  wire signal
  syntax: assign <signal> = <expression>;

## Slide 41: Exercise with SystemVerilog*
Implementation of a MUX and simulation with Modelsim
Continuous assignment
  wire signal
  syntax: assign <signal> = <expression>;

## Slide 42: Exercise with SystemVerilog
Implementation of a MUX and simulation with Modelsim
Continuous assignment
  wire signal
  syntax: assign <signal> = <expression>;
Ternary operator
    <condition> ? <if true> : <if false>
    sel ? … → sel == 1 ? …
      Non-zero value = true
      Zero value = false

## Slide 43: Exercise with SystemVerilog*
Implementation of a MUX and simulation with Modelsim
Blocking assignment
  reg signal
  always_comb block
  operator =

## Slide 44: Exercise with SystemVerilog*
Implementation of a MUX and simulation with Modelsim
Blocking assignment
  reg signal
  always_comb block
  operator =

## Slide 45: Exercise with SystemVerilog
Implementation of a MUX and simulation with Modelsim
Blocking assignment
  reg signal
  always_comb block
  operator =
if-else statement:
    if (<condition>)
      <assignment>
    else
      <assignment>

## Slide 46: Exercise with SystemVerilog
Implementation of a MUX and simulation with Modelsim
case statement:
    case (<signal>)
      <case value 1> : <assignment>;
      <case value 2> : <assignment>;
      …
    endcase

## Slide 47: Exercise with SystemVerilog
Implementation of a MUX and simulation with Modelsim
case statement:
    case (<signal>)
      <case value 1> : <assignment>;
      <case value 2> : <assignment>;
      …
    endcase
  if not all the cases are specified, the default case must be included:
      …
      default: <assignment>;
    endcase

## Slide 48: Exercise with SystemVerilog
Implementation of a MUX and simulation with Modelsim
Constants
  syntax: <bit width>’<base><value>
  examples:
    2’b00
    4’d0
    16’hFA3E
    …

## Slide 49: Exercise with SystemVerilog
Implementation of a MUX and simulation with Modelsim
Constants
  syntax: <bit width>’<base><value>
    b = binary
    d = decimal
    h = hexadecimal

## Slide 50: Exercise with SystemVerilog
Additional note
  If any of the previous assignment blocks (i.e., always_comb, if-else, case value) contains more than one assignment, the begin – end delimiters must be used

## Slide 51: Exercise with SystemVerilog
Implementation of a MUX and simulation with Modelsim
  You can find all the files about this exercise in the dedicated folder on the Team of the course
    File > Electronics Systems module > Crocetti > Exercises > 2.1
  Try to simulate the different implementations of the MUX with Modelsim
    Refer to Lecture 1.2