## Slide 1: Electronics Systems (938II)
Lecture 2.2
Building Blocks of Electronic Systems – Arithmetic operations

## Slide 2: Combinational circuits for arithmetic operations*
Let’s assume arithmetic operations on integers (with sign)
  Addition
  Subtraction
  Multiplication
  Division
For this purpose, integers are represented using two’s complement (C2)

## Slide 3: Two’s complement representation (of integers with sign)*
Assume N bits
  Most significant bit (MSB), the leftmost one, is the sign bit
MSB
LSB
(sign bit)
…
N-1
N-2
N-3
0
1

## Slide 4: Two’s complement representation (of integers with sign)*
Positive numbers
  Natural binary representation
  Sign bit = 0
  Example: 1 → 000…01
…
0
0
0
1
0
1 (decimal base)

## Slide 5: Two’s complement representation (of integers with sign)*
Negative numbers
  Get absolute binary representation (i.e. corresponding positive value)
  Invert (or complement) all bits
  Add 1 (ignoring overflow)

## Slide 6: Two’s complement representation (of integers with sign)*
Negative numbers
  Get absolute binary representation (i.e. corresponding positive value)
  Invert (or complement) all bits
  Add 1 (ignoring overflow)
  Example: –1

## Slide 7: Two’s complement representation (of integers with sign)*
…
Negative numbers
  Get absolute binary representation (i.e. corresponding positive value)
  Invert (or complement) all bits
  Add 1 (ignoring overflow)
  Example: –1
0
0
0
1
0
1 (decimal base)

## Slide 8: Two’s complement representation (of integers with sign)*
…
Negative numbers
  Get absolute binary representation (i.e. corresponding positive value)
  Invert (or complement) all bits
  Add 1 (ignoring overflow)
  Example: –1
0
0
0
1
0
1 (decimal base)
…
1
1
1
0
1

## Slide 9: Two’s complement representation (of integers with sign)*
…
Negative numbers
  Get absolute binary representation (i.e. corresponding positive value)
  Invert (or complement) all bits
  Add 1 (ignoring overflow)
  Example: –1
0
0
0
1
0
1 (decimal base)
…
1
1
1
0
1
+
…
0
0
0
1
0
…
1
1
1
1
1
-1 (decimal base)

## Slide 10: Two’s complement representation (of integers with sign)*
Negative numbers
  Get absolute binary representation (i.e. corresponding positive value)
  Invert (or complement) all bits
  Add 1 (ignoring overflow)
  Example: –2

## Slide 11: Two’s complement representation (of integers with sign)*
…
Negative numbers
  Get absolute binary representation (i.e. corresponding positive value)
  Invert (or complement) all bits
  Add 1 (ignoring overflow)
  Example: –2
0
0
0
0
1
2 (decimal base)

## Slide 12: Two’s complement representation (of integers with sign)*
…
Negative numbers
  Get absolute binary representation (i.e. corresponding positive value)
  Invert (or complement) all bits
  Add 1 (ignoring overflow)
  Example: –2
0
0
0
0
1
2 (decimal base)
…
1
1
1
1
0

## Slide 13: Two’s complement representation (of integers with sign)*
…
Negative numbers
  Get absolute binary representation (i.e. corresponding positive value)
  Invert (or complement) all bits
  Add 1 (ignoring overflow)
  Example: –2
0
0
0
0
1
2 (decimal base)
…
1
1
1
1
0
+
…
0
0
0
1
0
…
1
1
1
0
1
-2 (decimal base)

## Slide 14: Two’s complement representation (of integers with sign)*
Range of signed integer numbers (in decimal base) =

## Slide 15: Two’s complement representation (of integers with sign)*
Range of signed integer numbers (in decimal base) =
C2 representation
011…11
…
000…01
000…00
111…11
111…01
…
100…00

## Slide 16: Two’s complement representation (of integers with sign)*
Range of signed integer numbers (in decimal base) =
  Example:

## Slide 17: Two’s complement representation (of integers with sign)*
Range of signed integer numbers (in decimal base) =
  Example:
C2 representation | Decimal base
011 | 3
010 | 2
001 | 1
000 | 0
111 | -1
110 | -2
101 | -3
100 | -4

## Slide 18: Two’s complement representation (of integers with sign)*
Why this?
  Because it allows to perform arithmetic operations without particular (or dedicated) resources to handle the sign
    Lower costs
    Lower delays
    Subtraction can be implemented as the addition with the opposite number; for examples …
      10 – 18 = 10 + (-18)
      12 – (-7) = 12 + 7
      …
Let’s see some examples
  Assuming N = 3 bits

## Slide 19: Two’s complement representation (of integers with sign)*
0
1
0
+
0
1
0
0
0
1
(1)
(1)
(2)
0
1
0
+
1
1
1
0
0
0
(1)
(-1)
(0)
0
1
0
+
1
0
1
1
1
1
(1)
(-2)
(-1)
1
1
1
+
1
1
1
1
0
1
(-1)
(-1)
(-2)
1
0
1
+
1
0
1
1
0
0
(-2)
(-2)
(-4)
1
0
1
+
0
1
1
0
1
0
(-2)
(3)
(1)
1 + 1
1 + (-1) → 1 – 1
1 + (-2) → 1 – 2
-1 + (-1) → -1 – 1
-2 + (-2) → -2 – 2
-2 + 3 → 3 – 2

## Slide 20: Adder*
The sum of 2 N-bit numbers requires N+1 bits to be represented
  N = 1 → 2 bits to represent the sum
The simplest adder is the Half Adder (HA)
  Just the sum of the two 1-bit inputs (a, b)
  Output must be 2-bit

## Slide 21: Adder*
The sum of 2 N-bit numbers requires N+1 bits to be represented
  N = 1 → 2 bits to represent the sum
The simplest adder is the Half Adder (HA)
  Just the sum of the two 1-bit inputs (a, b)
  Output must be 2-bit
    s
    = carry (output)

## Slide 22: Half Adder (HA)*
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
HA truth table

## Slide 23: Half Adder (HA)*
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
HA truth table
, when

## Slide 24: Half Adder (HA)*
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
HA truth table
, when

## Slide 25: Half Adder (HA)*
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
HA truth table
, when

## Slide 26: Half Adder (HA)*
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
HA truth table
, when
, when
and

## Slide 27: Half Adder (HA)*
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
HA truth table
, when
, when
and

## Slide 28: Half Adder (HA)*
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
HA truth table
, when
, when
and

## Slide 29: Adder*
But, as we saw earlier, when summing two multi-bit vectors, it may happen that the carry is generated by the sum of the previous bits
  To fully support the addition, also a carry input must be considered
    = carry (input)
  The corresponding (1-bit) adder is called Full Adder (FA)

## Slide 30: Full Adder (FA)*
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
FA truth table

## Slide 31: Full Adder (FA)*
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
FA truth table

## Slide 32: Full Adder (FA)*

## Slide 33: Adder (for multi-bit operands)*
A generic adder (for N-bit operands) can be built by cascading N FAs
  Example: 4-bit adders
    Inputs
      a = {a3 a2 a1 a0}
      b = {b3 b2 b1 b0}
      cin
    Outputs
      s = {s3 s2 s1 s0}
      cout

## Slide 34: Adder (for multi-bit operands)*
The one saw before is called also Ripple Carry Adder (RCA)
  The carry path propagate from the input to the output
    Path is proportional to the bit width of the input operands
    The delay path may be very high
  Other solutions (and architectures/circuits) for adders exist to solve this problem
    Carry Save Adder (CSA)
    Carry Bypass Adder (CBA), or Carry Skip Adder
    Carry Lookahead Adder (CLA)

## Slide 35: Adder (for multi-bit operands)*
CSA, CBA, CLA, …: just for the sake of completeness
  We are not going to analyze them
  However, remember that each solution is a trade-off
    They can be advantageous in terms of delay with respect to the RCA
    But they can also present costs in other terms (e.g., resources)

## Slide 36: Subtractor (for multi-bit operands)*
If you remember the properties of two’s complement representation…
  A – B = A + (-B)

## Slide 37: Adder/Subtractor (for multi-bit operands)*
For a full-case solution, i.e. adder/subtractor
  Inputs : A, B
  Control : sub
    If sub = 0 → A + B
    If sub = 1 → A – B = A + (-B)

## Slide 38: Adder/Subtractor (for multi-bit operands)*
For a full-case solution, i.e. adder/subtractor
  If you remember, to get -B from B:
    Complement all bits of B
    Add 1
      This can be done by exploiting the input of RCA

## Slide 39: Adder/Subtractor (for multi-bit operands)*
For a full-case solution, i.e. adder/subtractor
  If you remember, to get -B from B:
    Complement all bits of B
    Add 1
      This can be done by exploiting the input of RCA

## Slide 40: Multiplier*
The multiplication of a N-bit number by an M-bit number requires N+M bits to be represented
  Typically, N = M → 2N bits to represent the product
The simplest way: shift-and-add algorithm
  Similar to the paper-and-pencil method for decimal multiplication

## Slide 41: Multiplier*
Assume N = 4 and calculate p = a * b
  a = {a3 a2 a1 a0}
  b = {b3 b2 b1 b0}
  p

## Slide 42: Multiplier*
Assume N = 4 and calculate p = a * b
  a = {a3 a2 a1 a0}
  b = {b3 b2 b1 b0}
  p

## Slide 43: Multiplier*
Assume N = 4 and calculate p = a * b
  a = {a3 a2 a1 a0}
  b = {b3 b2 b1 b0}
  p
  N – 1 additions of numbers with a bit width of 2N – 1 Sequential multiplier
0
0
0
0
0
0
0
0
0
0
0
0

## Slide 44: Sequential multiplier*
Logic for calculation of AND products
One adder
  The RCA we saw before
A register to store partial products
Requiring N – 1 steps/cycles to perform the multiplication

## Slide 45: Combinational multiplier
Example: N = 4

## Slide 46: Combinational multiplier
Example: N = 4
  3x 4-bit RCAs
In general
  N – 1x RCAs
  Each of N bits
Plus logic for AND!!!

## Slide 47: Divisor*
Similarly to multiplier, the divisor can be implemented exploiting again an adder (RCA) supporting two’s complement addition
  Division can be split in a sequence of subtractions and comparison
  Example: 63 / 12
    Quotient = 0
    63 – 12 = 51 → Quotient += 1 (1), 51 > 12 ? Yes
    51 – 12 = 39 → Quotient += 1 (2), 39 > 12 ? Yes
    39 – 12 = 27 → Quotient += 1 (3), 13 > 12 ? Yes
    27 – 12 = 15 → Quotient += 1 (4), 15 > 12 ? Yes
    15 – 12 = 3 → Quotient += 1 (5), 3 > 12 ? No → Reminder = 3
  Or other combinational circuits can be implemented

## Slide 48: Multiplicator/Divisor*
We are not going to see the circuit of a combinational divisor, however …
… remember that multipliers and divisors are expansive
  Resources and/or time (steps/cycles)

## Slide 49: Combinational logic in modern processors*
If you remember the overall outline of a modern processor

## Slide 50: Combinational logic in modern processors*
The main component of the Combinational logic block is called ALU
  ALU = Arithmetic Logic Unit

## Slide 51: ALU*
Main operations (but not all) supported by an ALU
OPCODE (select) |  | Meaning
ADD | 00001 | A + B
SUB | 00010 | A – B
MULT | 01000 | A * B
NOT | 10000 | Complement A
AND | 10001 | Bit-wise AND
OR | 10010 | Bit-wise OR
XOR | 10011 | Bit-wise XOR
EQL | 01011 | Check A == B
… | … | …

## Slide 52: ALU*
Therefore, a possible architecture for an ALU can be the following one

## Slide 53: ALU*
Therefore, a possible architecture for an ALU can be the following one
  Basic logic gates

## Slide 54: ALU*
Therefore, a possible architecture for an ALU can be the following one
  Basic logic gates
  Multiplexers

## Slide 55: ALU*
Therefore, a possible architecture for an ALU can be the following one
  Basic logic gates
  Multiplexers
  XOR/Comparator

## Slide 56: ALU*
Therefore, a possible architecture for an ALU can be the following one
  Basic logic gates
  Multiplexers
  XOR/Comparator
  Adder/Subtractor

## Slide 57: Exercise with SystemVerilog
Implementation of a 4-bit Adder and simulation with Modelsim

## Slide 58: Exercise with SystemVerilog
Implementation of a 4-bit Adder and simulation with Modelsim

## Slide 59: Exercise with SystemVerilog
Implementation of a 4-bit Adder and simulation with Modelsim

## Slide 60: Exercise with SystemVerilog
Implementation of a 4-bit Adder and simulation with Modelsim
Continuous assignment (again)
  assign <signal> = <expression>;
  But using arithmetic operator (+) in <expression>

## Slide 61: Exercise with SystemVerilog
Implementation of a 4-bit Adder and simulation with Modelsim
Some operators in SV
  Arithmetic
    They can be use in any expression/assignment (also blocking or non-blocking)
    Addition +
    Subtraction –
    Multiplication *
    Division /
    Power ** (e.g., a**b = )
    Mod % (e.g., a % b = a mod b)

## Slide 62: Exercise with SystemVerilog
Implementation of a 4-bit Adder and simulation with Modelsim
Some operators in SV
  Bit-wise
    They can be use in any expression/assignment (also blocking or non-blocking)
    AND &
    OR |
    NOT ~

## Slide 63: Exercise with SystemVerilog
Implementation of a 4-bit Adder and simulation with Modelsim
Some operators in SV
  Logical
    They can be used in any control condition (if–else, ternary operator)
    AND &&
    OR ||
    NOT !

## Slide 64: Exercise with SystemVerilog
Implementation of a 4-bit Adder and simulation with Modelsim
Some operators in SV
  Relational
    They can be used in any control condition (if–else, ternary operator)
    Equality ==
    Inequality !=
    Greater than >
    Greater than or equal >=
    Lower than <
    Lower than or equal <=

## Slide 65: Exercise with SystemVerilog
Implementation of a 4-bit Adder and simulation with Modelsim
Try to simulate it on Modelsim with the force and run command
  To assign a multi-bit value with the force command use the syntax for constants in SV
    force a 4’d0
    force b 4’d3
    …

## Slide 66: Exercise with SystemVerilog
Implementation of a 4-bit Adder and simulation with Modelsim
Try to simulate it on Modelsim with the force and run command
  A suggestion: to plot the waveform, use the Unsigned radix (for a, b, and c)

## Slide 67: Exercise with SystemVerilog
Implementation of a 4-bit Adder and simulation with Modelsim
  Signed version: supporting two’s complement operands
Signals must be declared as signed
  By default, all signals are unsigned

## Slide 68: Exercise with SystemVerilog
Implementation of a 4-bit Adder and simulation with Modelsim
  Signed version: supporting two’s complement operands
Signals must be declared as signed
  By default, all signals are unsigned
  It applies to both ports and internal signals

## Slide 69: Exercise with SystemVerilog
Implementation of a 4-bit Adder and simulation with Modelsim
  Signed version: supporting two’s complement operands
Signals must be declared as signed
  By default, all signals are unsigned
  It applies to both ports and internal signals
    It must be specified after the type

## Slide 70: Exercise with SystemVerilog
Implementation of a 4-bit Adder and simulation with Modelsim
  Signed version: supporting two’s complement operands
Try to simulate it on Modelsim with the force and run command
  To assign negative value with the force command use …
    force a –4’d1
    force b –4’d3
    …
    Remember of representable range!!!

## Slide 71: Exercise with SystemVerilog
Implementation of a 4-bit Adder and simulation with Modelsim
  Signed version: supporting two’s complement operands
Try to simulate it on Modelsim with the force and run command
  A suggestion: to plot the waveform, use the Decimal radix (for a, b, and c)

## Slide 72: Exercise with SystemVerilog
Implementation of a 4-bit Adder and simulation with Modelsim
  You can find all the files about this exercise in the dedicated folder on the Team of the course
    File > Electronics Systems module > Crocetti > Exercises > 2.2
  Try to simulate on your own both unsigned and signed version of the 4-bit adder
    Unsigned version → ‘adder_4_bit’
    Signed version → ‘adder_c2_4_bit’

## Slide 73: Exercise with SystemVerilog
Implementation of a 4-bit Adder and simulation with Modelsim
  For the signed version, you can find ‘adder_c2_4_bit’ two auxiliary .do files
    ‘wave_adder_c2.do’
    ‘sim_adder_c2.do’
    Refer to README.txt file
    However, you can run them using again the Transcript Tab and the do command
      After having launched the simulation
wave_adder_c2.do
sim_adder_c2.do