## Slide 1: Electronics Systems (938II)
Lecture 2.3
Building Blocks of Electronic Systems – Latch, Flip-flop, Register

## Slide 2: Sequential logic*
Sequential circuits that have “memory”, because its output depends on
  Current input(s)
  Previous output
    Defined as current state
Already mentioned in previous lectures, the most notorious and used sequential circuit is the register
  Store data

## Slide 3: Sequential logic*
A register consists of one (or more)
  D flip-flop (or DFF)
  The D flip-flop is built upon the D latch
  The D latch is built upon the SR latch, that can be easily built using CMOS gates

## Slide 4: Sequential logic*
A register consists of one (or more)
  D flip-flop (or DFF)
  The D flip-flop is built upon the D latch
  The D latch is built upon the SR latch, that can be easily built using CMOS gates
Let’s see how they are made, starting from the base, the SR latch!

## Slide 5: SR latch*
Can be defined as a circuit that
  Takes in input the signals S and R
    S = Set
    R = Reset
  Has output(s)
  According to the inputs name
    When S = 1 and R = 0 → set command → output = 1
    When S = 0 and R = 1 → reset (or clear) command → output = 0
    Otherwise → keep previous output (= latch)

## Slide 6: SR latch*
Recalling functionality
  S = 1, R = 0 → output = 1
  S = 0, R = 1 → output = 0
  Otherwise → latch
  Please, note that
    is the complement (or binary inverse) of S
    is the complement (or binary inverse) of R

## Slide 7: SR latch*
Recalling functionality
  S = 1, R = 0 → output = 1
  S = 0, R = 1 → output = 0
  Otherwise → latch
  Please, note that
    is the complement (or binary inverse) of S
    is the complement (or binary inverse) of R
0 | 1 | 1 | 0
0 | 1 | 1 | 0
Set command (as expected)

## Slide 8: SR latch*
Recalling functionality
  S = 1, R = 0 → output = 1
  S = 0, R = 1 → output = 0
  Otherwise → latch
  Please, note that
    is the complement (or binary inverse) of S
    is the complement (or binary inverse) of R
0 | 1 | 1 | 0
1 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
Set command (as expected)
Reset command (as expected)

## Slide 9: SR latch*
Recalling functionality
  S = 1, R = 0 → output = 1
  S = 0, R = 1 → output = 0
  Otherwise → latch
  Please, note that
    is the complement (or binary inverse) of S
    is the complement (or binary inverse) of R
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | ?? | ??
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | ?? | ??
Set command (as expected)
Reset command (as expected)

## Slide 10: SR latch*
Recalling functionality
  S = 1, R = 0 → output = 1
  S = 0, R = 1 → output = 0
  Otherwise → latch
  Please, note that
    is the complement (or binary inverse) of S
    is the complement (or binary inverse) of R
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | ?? | ??
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | ?? | ??
Set command (as expected)
Reset command (as expected)
Assumption #1

## Slide 11: SR latch*
Recalling functionality
  S = 1, R = 0 → output = 1
  S = 0, R = 1 → output = 0
  Otherwise → latch
  Please, note that
    is the complement (or binary inverse) of S
    is the complement (or binary inverse) of R
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | ?? | ??
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | ?? | ??
Set command (as expected)
Reset command (as expected)
Assumption #2

## Slide 12: SR latch*
Recalling functionality
  S = 1, R = 0 → output = 1
  S = 0, R = 1 → output = 0
  Otherwise → latch
  Please, note that
    is the complement (or binary inverse) of S
    is the complement (or binary inverse) of R
  Both assumptions hold. In other words, when () and (), the latch keep the previous output(s): and
    And in both cases = inverse of
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 |  | 
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 |  | 
Set command (as expected)
Reset command (as expected)
Latch (as expected)

## Slide 13: SR latch*
Recalling functionality
  S = 1, R = 0 → output = 1
  S = 0, R = 1 → output = 0
  Otherwise → latch
  Please, note that
    is the complement (or binary inverse) of S
    is the complement (or binary inverse) of R
  In this case, and are forced to 1, and, in addition, = !!!
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 |  | 
0 | 0 | 1 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 |  | 
0 | 0 | 1 | 1
Set command (as expected)
Reset command (as expected)
Latch (as expected)
Forbidden! ()

## Slide 14: SR latch with Enable*
Let’s add and enable signal (EN) to the SR latch
  SR latch with Enable

## Slide 15: SR latch with Enable*
Looking at the circuit
  A = of SR latch
  B = of SR latch
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 |  | 
0 | 0 | 1 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 |  | 
0 | 0 | 1 | 1
SR latch truth table
SR latch

## Slide 16: SR latch with Enable*
Looking at the circuit
  A = of SR latch
  B = of SR latch
If EN = 0, A = 1 and B = 1
  and → SR latch: latch state
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 |  | 
0 | 0 | 1 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 |  | 
0 | 0 | 1 | 1
SR latch truth table
SR latch

## Slide 17: SR latch with Enable*
Looking at the circuit
  A = of SR latch
  B = of SR latch
If EN = 0, A = 1 and B = 1
  and → SR latch: latch state
If EN = 1
  It behaves the same as before!
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 |  | 
0 | 0 | 1 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 |  | 
0 | 0 | 1 | 1
SR latch truth table
SR latch

## Slide 18: SR latch with Enable*
If EN = 0, A = 1 and B = 1
  and → SR latch: latch state
If EN = 1
  It behaves the same as before!
0 | 1 | 1 | X | X |  | 
1 | 0 | 1 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0 | 1
1 | 1 | 1 | 0 | 0 |  | 
1 | 0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 1 | X | X |  | 
1 | 0 | 1 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0 | 1
1 | 1 | 1 | 0 | 0 |  | 
1 | 0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 |  | 
0 | 0 | 1 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 |  | 
0 | 0 | 1 | 1
SR latch truth table
SR latch

## Slide 19: SR latch with Enable*
Recap
0 | X | X |  | 
1 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 0 | 0 |  | 
1 | 1 | 1 | 1 | 1
0 | X | X |  | 
1 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 0 | 0 |  | 
1 | 1 | 1 | 1 | 1
Truth table of SR latch with Enable
Set command (as expected: S = 1, R = 0)
Reset command (as expected: S = 0, R = 1)
Latch (as expected: S = 0 and R = 0)
Forbidden! ()
Latch (because ‘disabled’: EN = 0)

## Slide 20: D latch*
Can be defined as a circuit that
  Takes in input the signals D and EN
    D = Data
    EN = Enable
  Has output(s)
  Has then following functionality:
    When EN = 0 → latch (keep previous output(s))
    When EN = 1 → D sets the primary output (Q): Q = D

## Slide 21: D latch*
It can be built using the SR latch with Enable
  When EN = 0 → latch
  When EN = 1 → D sets the primary output (Q): Q = D
    D = 1 → Q = 1 → S = 1, R = 0
    D = 0 → Q = 0 → S = 0, R = 1

## Slide 22: D latch*
It can be built using the SR latch with Enable
  When EN = 0 → latch
  When EN = 1 → D sets the primary output (Q): Q = D
    D = 1 → Q = 1 → S = 1, R = 0
    D = 0 → Q = 0 → S = 0, R = 1
S = D
R =

## Slide 23: D latch*

## Slide 24: D latch*
SR latch with Enable
0 | X | X |  | 
1 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 0 | 0 |  | 
1 | 1 | 1 | 1 | 1
0 | X | X |  | 
1 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 0 | 0 |  | 
1 | 1 | 1 | 1 | 1
Truth table of SR latch with Enable

## Slide 25: D latch*
SR latch with Enable
0 | X | X |  | 
1 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 0 | 0 |  | 
1 | 1 | 1 | 1 | 1
0 | X | X |  | 
1 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 0 | 0 |  | 
1 | 1 | 1 | 1 | 1
Truth table of SR latch with Enable
If EN = 0, it acts like before (SR latch with Enable)
If EN = 1
  If D = 0 → S = 0 and R = 1 → Reset command (Q = 0)
  If D = 1 → S = 1 and R = 0 → Set command (Q = 1)

## Slide 26: D latch*
EN | D |  | 
0 | X |  | 
1 | 0 | 0 | 1
1 | 1 | 1 | 0
EN | D |  | 
0 | X |  | 
1 | 0 | 0 | 1
1 | 1 | 1 | 0
(Truth table)
(Gate-level)

## Slide 27: D latch*
In addition, the forbidden condition of the SR latch never occurs
  Thanks to the NOT gate, whatever the value of D, it happens that
    Either S = 1 and R = 0
    Or S = 0 and R = 1
  It can never happen neither S = 0 and R = 0, nor S = 1 and R = 1
EN | D |  | 
0 | X |  | 
1 | 0 | 0 | 1
1 | 1 | 1 | 0
EN | D |  | 
0 | X |  | 
1 | 0 | 0 | 1
1 | 1 | 1 | 0
(Truth table)
(Gate-level)

## Slide 28: D latch*
Logic symbol(s)
EN | D |  | 
0 | X |  | 
1 | 0 | 0 | 1
1 | 1 | 1 | 0
EN | D |  | 
0 | X |  | 
1 | 0 | 0 | 1
1 | 1 | 1 | 0
(Truth table)
(Gate-level)
(RTL)

## Slide 29: D flip-flop (or DFF)*
As any other flip-flop, it is built by cascading two latches (of the same type)
  Two D latches in this case
Let’s see what happen by using a waveform
Q

## Slide 30: D flip-flop (or DFF)*
Q

## Slide 31: D flip-flop (or DFF)*
When EN1 = CLK is 1, Q1 = D
Q

## Slide 32: D flip-flop (or DFF)*
When EN1 = CLK is 1, Q1 = D
Otherwise, M latches and keep the last value of Q1
Q

## Slide 33: D flip-flop (or DFF)*
Similarly, it happens for DFF2, but EN2 is the inverse of CLK
  NOT gate
So, …
Q

## Slide 34: D flip-flop (or DFF)*
When CLK = 0, EN2 = 1, Q = Q1
  Q1 is the data input of S
Q

## Slide 35: D flip-flop (or DFF)*
When CLK = 0, EN2 = 1, Q = Q1
  Q1 is the data input of S
Otherwise, S latches and keep the last value of Q2
Q

## Slide 36: D flip-flop (or DFF)*
In other words, the (primary) output of the DFF, i.e. Q, changes only at the falling edges of the signal CLK
Q

## Slide 37: D flip-flop (or DFF)*
CLK signal is typically called clock signal, and it is a periodic signal which oscillates between 0 and 1
Since the DFF is ‘activated’ by the (falling) edge of CLK, it said to be edge-triggered
  In particular, negative-edge-triggered, since it is sensitive to the falling edge of clock signal

## Slide 38: D flip-flop (or DFF)*
CLK signal is typically called clock signal, and it is a periodic signal which oscillates between 0 and 1
Since the DFF is ‘activated’ by the (falling) edge of CLK, it said to be edge-triggered
  In particular, negative-edge-triggered, since it is sensitive to the falling edge of clock signal
Negative-edge-triggered D flip-flop
Q

## Slide 39: D flip-flop (or DFF)*
CLK signal is typically called clock signal, and it is a periodic signal which oscillates between 0 and 1
Since the DFF is ‘activated’ by the (falling) edge of CLK, it said to be edge-triggered
  In particular, negative-edge-triggered, since it is sensitive to the falling edge of clock signal
  A positive-edge-triggered DFF (sensitive to the rising edge of the clock signal) can be obtained by inverting CLK at the input with another NOT gate
Negative-edge-triggered D flip-flop
Q

## Slide 40: D flip-flop (or DFF)*
CLK signal is typically called clock signal, and it is a periodic signal which oscillates between 0 and 1
Since the DFF is ‘activated’ by the (falling) edge of CLK, it said to be edge-triggered
  In particular, negative-edge-triggered, since it is sensitive to the falling edge of clock signal
  A positive-edge-triggered DFF (sensitive to the rising edge of the clock signal) can be obtained by inverting CLK at the input with another NOT gate
Negative-edge-triggered D flip-flop
Q
Positive-edge-triggered D flip-flop
Q

## Slide 41: D flip-flop (or DFF)*
This architecture was historically called Master-Slave architecture
  Leftmost latch = Master, rightmost latch = Slave
  It cannot be longer used for ethical reasons
  Saying only because in case of further investigation you are very likely to find more matches using this historical name
  Current name is Primary-Secondary (respectively)
Negative-edge-triggered D flip-flop
Positive-edge-triggered D flip-flop
Q
Q

## Slide 42: D flip-flop (or DFF)*
Negative-edge-triggered D flip-flop
Positive-edge-triggered D flip-flop
Functional symbol = logic symbol
Functional symbol = logic symbol
Q
Q

## Slide 43: D flip-flop (or DFF)*
Please note that the logic symbol of a flip-flop has an empty triangle on the signal used as clock!
  This to indicate that that input is sensitive to the edge of the connected signal
  Not to the level (as in the case of latches)
Positive-edge-triggered: active on the rising edge (of CLK)
Negative-edge-triggered: active on the falling edge (of CLK)
Positive-level-sensitive: active when EN = 1
Negative-level-sensitive: active when EN = 0

## Slide 44: D flip-flop (or DFF)*
For this reason, typically the (triggering) edge of the clock signal is indicated in the truth table of the DFF
Negative-edge-triggered D flip-flop
Positive-edge-triggered D flip-flop
D | CLK |  | 
0 |  | 0 | 1
1 |  | 1 | 0
X | 0 |  | 
X | 1 |  | 
D | CLK |  | 
0 |  | 0 | 1
1 |  | 1 | 0
X | 0 |  | 
X | 1 |  | 
D | CLK |  | 
0 |  | 0 | 1
1 |  | 1 | 0
X | 0 |  | 
X | 1 |  | 
D | CLK |  | 
0 |  | 0 | 1
1 |  | 1 | 0
X | 0 |  | 
X | 1 |  | 

## Slide 45: D flip-flop (or DFF)*
Typically, the positive-edge-triggered D flip-flop is the most used one
  For this reason, it is generally indicated as just flip-flop
  When one hears of a flip-flop, one implicitly refers to a D flip-flop
Additional solutions exist (for both edge-triggered DFFs) that count
  An asynchronous reset (or clear): CLR
    To reset the DFF regardless of clock signal (an its activating edge)
  An asynchronous preset: PRE
    To preliminary set to 1 the DFF output regardless of clock signal (an its activating edge)
  They are typically active-low signals

## Slide 46: Register*
Finally, we can define what is a Register
  A register is a group of D flip-flops that store a binary value and share the same clock signal
  The number of DFFs depends on the bit width of the value to be stored
    N bits → N DFFs

## Slide 47: Register*
Some examples
  Omitting
1-bit register
4-bit register

## Slide 48: Register*
Functional symbol

## Slide 49: Register*
Functional symbol
  For simplicity, in RTL schematics you can find the following simplified symbols
    I will do the same in the next lectures

## Slide 50: Register*
Since the change of the register state occurs on a periodic signal (the clock), the register is a synchronous circuit
  As well as DFF
Like DFFs, registers can also have an asynchronous reset!
  Which is shared between all the DFFs composing the register

## Slide 51: Exercise with SystemVerilog
Implementation of an 8-bit Register and simulation with Modelsim

## Slide 52: Exercise with SystemVerilog
Implementation of an 8-bit Register and simulation with Modelsim

## Slide 53: Exercise with SystemVerilog*
Implementation of an 8-bit Register and simulation with Modelsim
Non-blocking assignment
  reg signal
  always_ff block
    Triggering edge of the clock signal in the sensitivity list
  operator <=

## Slide 54: Exercise with SystemVerilog*
Implementation of an 8-bit Register and simulation with Modelsim
Non-blocking assignment
  reg signal
  always_ff block
    Triggering edge of the clock signal in the sensitivity list
  operator <=

## Slide 55: Exercise with SystemVerilog*
Non-blocking vs blocking assignment
Non-blocking assignment
  Evaluated in sequence
  But assigned only after all are evaluated
Blocking assignment
  Assigned ‘immediately’

## Slide 56: Exercise with SystemVerilog*
Non-blocking vs blocking assignment
Non-blocking assignment
  Evaluated in sequence
  But assigned only after all are evaluated
Blocking assignment
  Assigned ‘immediately’

## Slide 57: Exercise with SystemVerilog*
Non-blocking vs blocking assignment
Blocking assignment
  Assigned ‘immediately’

## Slide 58: Exercise with SystemVerilog*
Implementation of an 8-bit Register and simulation with Modelsim
Adding asynchronous reset
  port
  signal (edge) inside sensitivity list
    asynchronous w.r.t. to clock signal
    must activate the always_ff block regardless of the clock
    specify required edge
      negedge → active-low
      posedge → active-high

## Slide 59: Exercise with SystemVerilog*
Implementation of an 8-bit Register and simulation with Modelsim
Adding asynchronous reset
  port
  signal (edge) inside sensitivity list
    asynchronous w.r.t. to clock signal
    must activate the always_ff block regardless of the clock
    specify required edge
      negedge → active-low
      posedge → active-high

## Slide 60: Exercise with SystemVerilog*
Implementation of an 8-bit Register and simulation with Modelsim
Adding synchronous reset
  port
  but nothing more
    no signal (edge) in the sensitivity list
    also reset is synchronous to clock, so reset must not activate the always_ff block

## Slide 61: Exercise with SystemVerilog*
Register without reset
Register with asynchronous (active-low) reset
Register with asynchronous (active-high) reset
Register with synchronous (active-low) reset
Register with synchronous (active-high) reset

## Slide 62: Exercise with SystemVerilog
Implementation of an 8-bit Register and simulation with Modelsim
  You can find all the files about this exercise in the dedicated folder on the Team of the course
    File > Electronics Systems module > Crocetti > Exercises > 2.3
  Try to simulate on your own
  However, I also included two .do files to automate the waveform and the simulation
    wave.do and sim.do
    Refer to README.txt file