## Slide 1: Electronics Systems (938II)
Lecture 2.6
Building Blocks of Electronic Systems – Timing constraints

## Slide 2: Timing constraints*
Do you remember of registers and flip-flops?
  They are edge-triggered, i.e. the output change only on the triggering edge of the clock signal

## Slide 3: Timing constraints*
Do you remember of registers and flip-flops?
  To work properly, the input signal (D), must be stable
    A certain time interval before the (triggering) edge of clock
    A certain time interval after the (triggering) edge of clock

## Slide 4: Timing constraints*
Do you remember of registers and flip-flops?
  Otherwise, the register/flip-flop goes into a metastable state
    I.e., the output is unpredictable
    It oscillates for a while between 0 and 1, and then settles down to either 1 or 0

## Slide 5: Timing constraints*
Do you remember of registers and flip-flops?
  Otherwise, the register/flip-flop goes into a metastable state
    I.e., the output is unpredictable
    It oscillates for a while between 0 and 1, and then settles down to either 1 or 0

## Slide 6: Timing constraints*
Do you remember of registers and flip-flops?
  The interval time in which the input must be stable
    Before the triggering-edge of clock is called setup time:
    After the triggering-edge of clock is called hold time :

## Slide 7: Timing constraints*
To check whether the conditions on setup and hold times are met, any digital synchronous circuit can be split in register-to-register paths
  RTL representation of the circuit
Combinational
circuit

## Slide 8: Register-to-register path*
An example
  How many paths?

## Slide 9: Register-to-register path*
An example
  How many paths?
  4!

## Slide 10: Register-to-register path*
An example
  How many paths?
  4!
    1

## Slide 11: Register-to-register path*
An example
  How many paths?
  4!
    2

## Slide 12: Register-to-register path*
An example
  How many paths?
  4!
    3

## Slide 13: Register-to-register path*
An example
  How many paths?
  4!
    4

## Slide 14: Register-to-register path*
Setup and hold times refer to the path between input data and clock
Combinational
circuit

## Slide 15: Register-to-register path*
However, for this analysis, also other time intervals must also be considered
Combinational
circuit

## Slide 16: Register-to-register path*
However, for this analysis, also other time intervals must also be considered
  = propagation delay of combinational circuit between the registers
Combinational
circuit

## Slide 17: Register-to-register path*
However, for this analysis, also other time intervals must also be considered
  = clock-to-output time, i.e. the time required to settle a valid output on an output pin after a clock transition
Combinational
circuit

## Slide 18: Register-to-register path*
In addition
  The source register is called the launch register, and the corresponding clock signal is called the launch clock
Combinational
circuit

## Slide 19: Register-to-register path*
In addition
  The destination register is called the capture register, and the corresponding clock signal is called the capture clock
Combinational
circuit

## Slide 20: Register-to-register path*
Ideally, the launch and capture clocks are the same signal with a period , but let’s consider them as two distinct signals
  It depends on the circuit manufacturing process
  Trust me for a while
Combinational
circuit

## Slide 21: Timing constraints – Setup time*
Let’s start by determining the timing constraint on the setup time
  Let’s define the points
    A = the output pin of the launch register
    B = the input pin of the capture register
Combinational
circuit

## Slide 22: Timing constraints – Setup time*

## Slide 23: Timing constraints – Setup time*
If , the change of input to the capture register (B) falls in the setup time, so …

## Slide 24: Timing constraints – Setup time*

## Slide 25: Timing constraints – Setup time*

## Slide 26: Timing constraints – Setup time*

## Slide 27: Timing constraints – Setup time*

## Slide 28: Timing constraints – Setup time*

## Slide 29: Timing constraints – Setup time*

## Slide 30: Timing constraints – Setup time*

## Slide 31: Timing constraints – Setup time*
→

## Slide 32: Timing constraints – Setup time*
→

## Slide 33: Timing constraints – Setup time*
To be honest, the propagation delay can be characterized by a minimum and maximum value
Combinational
circuit

## Slide 34: Timing constraints – Setup time*

## Slide 35: Timing constraints – Setup time*

## Slide 36: Timing constraints – Setup time*
  Why the worst case () ?

## Slide 37: Timing constraints – Setup time*
  Why the worst case () ?
  Because if the circuit works in the worst conditions, for sure it works also in the other conditions: typical, best

## Slide 38: Timing constraints – Setup time*
Summarizing, the timing constraint on the setup time () is

## Slide 39: Timing constraints – Setup time and clock frequency*
Summarizing, the timing constraint on the setup time () is
The clock frequency is , so the clock frequency must satisfy

## Slide 40: Timing constraints – Setup time and clock frequency*
Therefore, the maximum frequency is:

## Slide 41: Timing constraints – Hold time*
Now let’s move to the timing constraint on the hold time
Combinational
circuit

## Slide 42: Timing constraints – Hold time*

## Slide 43: Timing constraints – Hold time*

## Slide 44: Timing constraints – Hold time*

## Slide 45: Timing constraints – Hold time*

## Slide 46: Timing constraints – Hold time*

## Slide 47: Timing constraints – Hold time*

## Slide 48: Timing constraints – Hold time*

## Slide 49: Timing constraints – Hold time*
→

## Slide 50: Timing constraints – Hold time*
→

## Slide 51: Timing constraints – Hold time*

## Slide 52: Timing constraints – Hold time*
  Again, worst case for the same reasons

## Slide 53: Timing constraints – Hold time*
Summarizing, the timing constraint on the hold time () is

## Slide 54: Timing constraints*
Summary
  Setup → →
  Hold →

## Slide 55: Timing constraints*
Summary
  Setup → →
  Hold →
Is it ALL the truth?

## Slide 56: Timing constraints*
Summary
  Setup → →
  Hold →
Is it ALL the truth? No!
  Some aspects are still missing

## Slide 57: Timing constraints*
Modern digital systems count a lot of transistors
  We saw about VLSI: transistor count
    In some case up to
  Part of these transistors are used for registers/flip-flops
  A single clock signal must reach (physically) many registers
    Ideally at the same time
    However, this is not physically possible (because of the high density of registers)

## Slide 58: Timing constraints*
The clock distribution is a very delicate aspect of the chip manufacturing process
  It constitutes a specific and dedicated step of the manufacturing process: CTS (Clock Tree Synthesis)
  They exist techniques to optimize the distribution of clock and equalize it as much as possible

## Slide 59: Timing constraints*
Anyway, is not physically possible to make the distance between the clock source and the clock port of registers equal for all the registers
And even if so, other (physical, and unpredictable) factors may cause delays on the clock between different registers
  Temperature variations
  Material imperfections
  …

## Slide 60: Timing constraints*
Therefore, the delay model should include also the delay between the launch clock and the capture clock
  It is called skew and typically indicated with δ
Combinational
circuit
δ

## Slide 61: Timing constraints
This slightly changes the previous constraints we determined
Combinational
circuit
δ

## Slide 62: Timing constraints
In addition, also the wires delay () should be considered
Combinational
circuit
δ

## Slide 63: Timing constraints
And they exist corner cases that we did not consider

## Slide 64: Timing constraints
And they exist corner cases that we did not consider
  Input paths
    Launch register misses
Combinational
circuit
Input
pin

## Slide 65: Timing constraints
And they exist corner cases that we did not consider
  Output paths
    Capture register misses
Combinational
circuit
Output
pin

## Slide 66: Timing constraints
Input and output paths would require a more accurate delay model
  = input delay (of the input pin)
  = output delay (of the output pin)
Combinational
circuit
δ
Input
pin
Combinational
circuit
Output
pin

## Slide 67: Timing constraints
And they exist corner cases that we did not consider
  Others
    Combinational logic misses Both registers miss (combinational path)
Combinational
circuit

## Slide 68: Timing constraints*
We are not going to analyze the more accurate delay models
However, remember that
  The timing analysis to check the setup and hold constraints are met is an essential part of the design process of a circuit
    It is automated and called STA = Static Timing Analysis
    It can be performed multiple times/at different level, since any step of the design process can add information about timing
      Gate-level → information about gate delays
      Transistor-level → information about delays of wires, pins, …

## Slide 69: Timing constraints*
Also remember that
  Setup violations
    Can be fixed during design phase
      Frequency lowering, insertion of pipeline(s) to reduce the path delay, …
    Can be fixed after the fabrication of the chip
      Frequency lowering
  Hold violations
    Can be fixed during design phase
      Inserting delay chains (e.g., cascade of NOT gates or buffers)
    Cannot be fixed after the fabrication of the chip!!!