## Slide 1: Electronics Systems (938II)
Lecture 3.1
Semiconductor Memories – Basic principles

## Slide 2: Memories*
They are another fundamental building block that is part of modern electronic systems
  Processors need memory to work
Most (if not almost all) memories in modern computers and electronic systems are semiconductor memories
  They exist(ed) also magnetic and optical memories or storage devices, but they are actually outdated or used only in very few applications

## Slide 3: (Semiconductor) Memories – Classification*
Access mode
  Random Access Memory (RAM)
  Sequential Access Memory (SAM)
Supported operation(s)
  Read-Only Memory (ROM)
  Read and Write Memory (RWM)

## Slide 4: (Semiconductor) Memories – Classification*
Data retention
  Volatile
    Non-permanent data
    Data is lost after the memory is turned off
  Non-volatile
    Permanent data
    Data is retained even when the memory is turned off

## Slide 5: Semiconductor Memories – Rationale*
We have already seen an example of semiconductor memory
  D flip-flop
    1x D flip-flop = 1 memory bit
    It is an example of memory which is volatile and RWM
D flip-flops are used as memory in computers, but they are expensive in terms of cost, cost per bit, …
  There are memories based on semiconductor technologies (such as CMOS) that achieve lower cost per bit or, in other words, higher density per silicon area

## Slide 6: Semiconductor Memories – Rationale*
These specialized memory technologies enable a memory cell (1 bit) to be made at a cost of about 1 transistor

## Slide 7: Semiconductor Memories – Rationale*
These specialized memory technologies enable a memory cell (1 bit) to be made at a cost of about 1 transistor
  If you remember, a 1-bit register (or 1 D flip-flop) is made of

## Slide 8: Semiconductor Memories – Rationale*
These specialized memory technologies enable a memory cell (1 bit) to be made at a cost of about 1 transistor
  If you remember, a 1-bit register (or 1 D flip-flop) is made of
    1x NOT gate
    2x D latches
Q

## Slide 9: Semiconductor Memories – Rationale*
These specialized memory technologies enable a memory cell (1 bit) to be made at a cost of about 1 transistor
  If you remember, a 1-bit register (or 1 D flip-flop) is made of
    1x NOT gate
    2x D latches
      Each D latch is made of
        4x NAND gates
        1x NOT gate
Q

## Slide 10: Semiconductor Memories – Rationale*
These specialized memory technologies enable a memory cell (1 bit) to be made at a cost of about 1 transistor
  If you remember, a 1-bit register (or 1 D flip-flop) is made of
    1x NOT gate
    2x D latches
      Each D latch is made of
        4x NAND gates
        1x NOT gate
Q

## Slide 11: Semiconductor Memories – Rationale*
These specialized memory technologies enable a memory cell (1 bit) to be made at a cost of about 1 transistor
  If you remember, a 1-bit register (or 1 D flip-flop) is made of
    1x NOT gate
    2x D latches
      Each D latch is made of
        4x NAND gates → 4x (4 transistors) = 16 transistors
        1x NOT gate → 1x (2 transistors) = 2 transistors

## Slide 12: Semiconductor Memories – Rationale*
These specialized memory technologies enable a memory cell (1 bit) to be made at a cost of about 1 transistor
  If you remember, a 1-bit register (or 1 D flip-flop) is made of
    1x NOT gate
    2x D latches
      Each D latch is made of → 18 transistor
        4x NAND gates → 4x (4 transistors) = 16 transistors
        1x NOT gate → 1x (2 transistors) = 2 transistors

## Slide 13: Semiconductor Memories – Rationale*
These specialized memory technologies enable a memory cell (1 bit) to be made at a cost of about 1 transistor
  If you remember, a 1-bit register (or 1 D flip-flop) is made of
    1x NOT gate → 1x (2 transistors) = 2 transistors
    2x D latches → 2x (18 transistors) = 36 transistors
      Each D latch is made of → 18 transistor
        4x NAND gates → 4x (4 transistors) = 16 transistors
        1x NOT gate → 1x (2 transistors) = 2 transistors

## Slide 14: Semiconductor Memories – Rationale*
These specialized memory technologies enable a memory cell (1 bit) to be made at a cost of about 1 transistor
  If you remember, a 1-bit register (or 1 D flip-flop) is made of 38 transistors!
    1x NOT gate → 1x (2 transistors) = 2 transistors
    2x D latches → 2x (18 transistors) = 36 transistors
      Each D latch is made of → 18 transistor
        4x NAND gates → 4x (4 transistors) = 16 transistors
        1x NOT gate → 1x (2 transistors) = 2 transistors

## Slide 15: Semiconductor Memories – Rationale*
These specialized memory technologies enable a memory cell (1 bit) to be made at a cost of about 1 transistor
  If you remember, a 1-bit register (or 1 D flip-flop) is made of 38 transistors!
This was an academic example
  A real-world CMOS D flip-flop consists of fewer transistors
  However, looking at a real-world CMOS technology (7 nm) …

## Slide 16: Semiconductor Memories – Rationale*
These specialized memory technologies enable a memory cell (1 bit) to be made at a cost of about 1 transistor
  If you remember, a 1-bit register (or 1 D flip-flop) is made of 38 transistors!
This was an academic example
  A real-world CMOS D flip-flop consists of fewer transistors
  However, looking at a real-world CMOS technology (7 nm) …
    Area of a NAND gate

## Slide 17: Semiconductor Memories – Rationale*
These specialized memory technologies enable a memory cell (1 bit) to be made at a cost of about 1 transistor
  If you remember, a 1-bit register (or 1 D flip-flop) is made of 38 transistors!
This was an academic example
  A real-world CMOS D flip-flop consists of fewer transistors
  However, looking at a real-world CMOS technology (7 nm) …
    Area of a NAND gate → area of 1 transistor

## Slide 18: Semiconductor Memories – Rationale*
These specialized memory technologies enable a memory cell (1 bit) to be made at a cost of about 1 transistor
  If you remember, a 1-bit register (or 1 D flip-flop) is made of 38 transistors!
This was an academic example
  A real-world CMOS D flip-flop consists of fewer transistors
  However, looking at a real-world CMOS technology (7 nm) …
    Area of a NAND gate → area of 1 transistor
    Area of a DFF

## Slide 19: Semiconductor Memories – Rationale*
These specialized memory technologies enable a memory cell (1 bit) to be made at a cost of about 1 transistor
  If you remember, a 1-bit register (or 1 D flip-flop) is made of 38 transistors!
This was an academic example
  A real-world CMOS D flip-flop consists of fewer transistors
  However, looking at a real-world CMOS technology (7 nm) …
    Area of a NAND gate → area of 1 transistor
    Area of a DFF →

## Slide 20: Semiconductor Memories – Rationale*
These specialized memory technologies enable a memory cell (1 bit) to be made at a cost of about 1 transistor
  If you remember, a 1-bit register (or 1 D flip-flop) is made of 38 transistors!
This was an academic example
  A real-world CMOS D flip-flop consists of fewer transistors
  However, looking at a real-world CMOS technology (7 nm) …
    Area of a NAND gate → area of 1 transistor
    Area of a DFF → → One DFF is about 21 transistors

## Slide 21: Semiconductor Memories – Rationale*
We are going to see different types of semiconductor memories
  All the main ones used in modern electronic systems

## Slide 22: Semiconductor Memories – Rationale*
We are going to see different types of semiconductor memories
  All the main ones used in modern electronic systems
But first, let's take a look at the outline of the architecture of semiconductor memories
  It is common to all of them

## Slide 23: Semiconductor Memories – Architecture outline*
The architecture of semiconductor memories has a matrix shape
  Two dimensions
  Bi-dimensional addressing

## Slide 24: Semiconductor Memories – Architecture outline*
The architecture of semiconductor memories has a matrix shape
  Two dimensions
  Bi-dimensional addressing
Why not a vector shape?
  For two main reason

## Slide 25: Semiconductor Memories – Architecture outline*
Compatibility with manufacturing process
  Semiconductor systems/devices are fabricated by processing a circular die of silicon (typically called wafer)
Wafer shape

## Slide 26: Semiconductor Memories – Architecture outline*
Compatibility with manufacturing process
  Semiconductor systems/devices are fabricated by processing a circular die of silicon (typically called wafer)
  Using a matrix shape, some parts of the wafer are wasted
Wafer shape

## Slide 27: Semiconductor Memories – Architecture outline*
Compatibility with manufacturing process
  Semiconductor systems/devices are fabricated by processing a circular die of silicon (typically called wafer)
  If a vector shape is used, more parts of the wafer are wasted
Wafer shape

## Slide 28: Semiconductor Memories – Architecture outline*
Resource cost
  Suppose that bits of address are required
    Vector shape
      Mono-dimensional addressing → addresses
    Matrix shape
      Bi-dimensional addressing
      Assuming to split as
        addresses for one dimension
        addresses for the other dimension
      Total: addresses

## Slide 29: Semiconductor Memories – Architecture outline*
Resource cost
  Suppose that bits of address are required
    Vector shape
      Resource cost = logic resources to decode addresses
    Matrix shape
      Resource cost = logic resources to decode addresses
    With →
    ???

## Slide 30: Semiconductor Memories – Architecture outline*
Resource cost
  Suppose that bits of address are required:

## Slide 31: Semiconductor Memories – Architecture outline*
Resource cost
  Suppose that bits of address are required:

## Slide 32: Semiconductor Memories – Architecture outline*
Resource cost
  Suppose that bits of address are required:

## Slide 33: Semiconductor Memories – Architecture outline*
Resource cost
  Suppose that bits of address are required:

## Slide 34: Semiconductor Memories – Architecture outline*
Resource cost
  Suppose that bits of address are required:

## Slide 35: Semiconductor Memories – Architecture outline*
Resource cost
  Suppose that bits of address are required:
    Some numeric examples
      → → → (NO)
      , → → → (YES)
      , → → → (YES)
      , → → → (YES)
      …

## Slide 36: Semiconductor Memories – Architecture outline*
Resource cost
  Suppose that bits of address are required:
    A more realistic example:
      1 Mbit of memory →
      Assume and
      → →

## Slide 37: Semiconductor Memories – Architecture outline*
Resource cost
  Suppose that bits of address are required:
    A more realistic example:
      1 Mbit of memory →
      Assume and
      → →
    In other words, assuming realistic examples, it happens that !!!

## Slide 38: Semiconductor Memories – Architecture outline*
Resource cost
  Suppose that bits of address are required:
    A more realistic example:
      1 Mbit of memory →
      Assume and
      → →
    In other words, assuming realistic examples, it happens that !!!
    Bi-dimensional addressing requires far fewer resources for address decoding !!!

## Slide 39: Semiconductor Memories – Architecture outline*
Draft

## Slide 40: Semiconductor Memories – Architecture outline*
Draft
  = Word Line

## Slide 41: Semiconductor Memories – Architecture outline*
Draft
  = Word Line
  = Bit Line

## Slide 42: Semiconductor Memories – Architecture outline*
Draft
  = Word Line
  = Bit Line
  Memory cell
    Typically contains 1 transistor
    Or something different, but with “similar” cost in terms of silicon area

## Slide 43: Semiconductor Memories – Architecture outline*
Draft
  To complete the architecture, they are required
    A row decoder (or x-decoder)
      For decoding the Word Line address
    A column decoder (or y-decoder)
      For decoding the Bit Line address

## Slide 44: Semiconductor Memories – Architecture outline*
Final
(Q)

## Slide 45: Semiconductor Memories – Architecture outline*
Final – Read-Only Memory
  But only for ROM
    Just output (Q)
(Q)

## Slide 46: Semiconductor Memories – Architecture outline*
Final – Read-Only Memory
  But only for ROM
    Just output (Q)
  In case of RWM, an I/O block is required
    And a Read/Write (R/W) signal
(Q)

## Slide 47: Semiconductor Memories – Architecture outline*
Final – Read-Write Memory (RWM)
  D = input data (bit)
  Q = output data (bit)
Q
D

## Slide 48: Semiconductor Memories – Architecture outline*
The architecture shown before is the one for single-bit memories
  Each memory cell store 1 bit
  Read or Write of 1 bit at a time
Multi-bit memories are built by connecting in parallel single-bit memories
  Assuming
    Number of memory cells = → bits of address
    Bit length = (bits)
  Memory is organized as
  Data (of bits) is called word

## Slide 49: Semiconductor Memories – Architecture outline*
Multi-bit memory:
  parallel single-bit block
  Each single bit block
    Contains (single-bit) memory cells
    That are arranged as a matrix of from
  Typically, is an integer multiple of 10, so that …
    → → k (kilo)
    → → M (Mega)
    → → G (Giga)

## Slide 50: Semiconductor Memories – Architecture outline*
Multi-bit memory:
  Example of a 32k x 8 memory
    32k = 25 * 210 = 215 → 15 bits for address
    b = 8 → 8 parallel single-bit-output memory blocks