## Slide 1: Electronics Systems (938II)
Lecture 3.2
Semiconductor Memories – ROM and PROM

## Slide 2: ROM*
ROM = Read-Only Memory
  However, this gives information only on the supported operation(s)
    I.e., read-only (not write)
  It does not give information on the access mode (random or sequential)
    Typically, this kind of memories supports random access
      I.e., any arbitrary address can be accessed immediately
    So, it is also a RAM
      Please, do not confuse with the computer memory typically called RAM, which is a RAM (from the perspective of access mode), but it is also a RWM (Read-Write Memory)

## Slide 3: ROM – Architecture*
Brief reminder of the structure of semiconductor memories
  = Word Line
  = Bit Line

## Slide 4: ROM – Architecture*
Brief reminder of the structure of semiconductor memories
  = Word Line
  = Bit Line
In case of ROM, the memory cell can be
  1 n-MOS transistor
  Empty

## Slide 5: ROM – Architecture*
Memory cell – n-MOS transistor
  = Word Line
  = Bit Line
  n-MOS
    D = Drain
    G = Gate
    S = Source

## Slide 6: ROM – Architecture*
Memory cell – n-MOS transistor
  = Word Line
  = Bit Line
  n-MOS
    D = Drain
    G = Gate
    S = Source
  To complete the architecture …

## Slide 7: ROM – Architecture*
Memory cell – n-MOS transistor
  = Word Line
  = Bit Line
  n-MOS
    D = Drain
    G = Gate
    S = Source
  R = Resistor
    Pull-up resistor: connect to VCC = high logic level (1)

## Slide 8: ROM – Architecture*
Memory cell – n-MOS transistor
  Principle of operation

## Slide 9: ROM – Architecture*
Memory cell – n-MOS transistor
  Principle of operation
    = 0
      n-MOS = OFF (open circuit)
      = 1 (because of pull-up resistor)

## Slide 10: ROM – Architecture*
Memory cell – n-MOS transistor
  Principle of operation
    = 0
      n-MOS = OFF (open circuit)
      = 1 (because of pull-up resistor)
    = 1
      n-MOS = ON (short circuit)
      = 0 (ground connection through the n-MOS)

## Slide 11: ROM – Architecture*
Memory cell – Empty
  Principle of operation
    = 0
      = 1 (because of pull-up resistor)
    = 1
      = 1 (because of pull-up resistor)

## Slide 12: ROM – Architecture*
Memory cell – Summary
  Principle of operation
Memory cell | Word Line () | Bit Line ()
With n-MOS | 0 (disabled) | 1
 | 1 (enabled) | 0
Empty | 0 (disabled) | 1
 | 1 (enabled) | 1
Memory cell |  | 
With n-MOS | 0 (disabled) | 1
 | 1 (enabled) | 0
Empty | 0 (disabled) | 1
 | 1 (enabled) | 1

## Slide 13: ROM – Architecture*
Integrating the row and column decoders to complete the architecture

## Slide 14: ROM – Architecture*
Integrating the row and column decoders to complete the architecture
  Example on a 2x4 ROM
    A = Address (3-bit)
    Q = single-bit output

## Slide 15: ROM – Architecture*
Integrating the row and column decoders to complete the architecture
  Example on a 2x4 ROM
    A = Address (3-bit)
    Q = single-bit output
    Assume cell (x,y)

## Slide 16: ROM – Architecture*
Integrating the row and column decoders to complete the architecture
  Example on a 2x4 ROM
    A = Address (3-bit)
    Q = single-bit output
    Assume cell (x,y)
    Assume to read cell (1,1)

## Slide 17: ROM – Architecture*
Integrating the row and column decoders to complete the architecture
  Example on a 2x4 ROM
    A = Address (3-bit)
    Q = single-bit output
    Assume cell (x,y)
    Assume to read cell (0,1)

## Slide 18: ROM – Architecture*
Integrating the row and column decoders to complete the architecture
  Example on a 2x4 ROM
    A = Address (3-bit)
    Q = single-bit output
    Assume cell (x,y)
    Assume to read cell (1,3)

## Slide 19: ROM – Architecture*
Integrating the row and column decoders to complete the architecture
  Example on a 2x4 ROM
    A = Address (3-bit)
    Q = single-bit output
    Assume cell (x,y)
    Assume to read cell (0,3)

## Slide 20: ROM – Architecture*
So, when reading (i.e. enabling corresponding word line and bit line) a memory cell
  With (n-MOS) transistor → Output = 0
  Empty (without transistor) → Output = 1
However, also solutions with active-low decoding logic (for column decoder) exist

## Slide 21: ROM – Architecture*
Active-low decoding logic (column decoder)
  Example on a 2x4 ROM

## Slide 22: ROM – Architecture*
Active-low decoding logic (column decoder)
  Example on a 2x4 ROM
    Assume to read cell (0,3)

## Slide 23: ROM – Architecture*
When reading a memory cell when column decoder is active-low
  With (n-MOS) transistor → Output = 1
  Empty (without transistor) → Output = 0
  The opposite of the previous case

## Slide 24: ROM – Architecture*
Content of memory cells
  The output (bit) corresponds to the content of memory cells, since that is what is obtained by reading that cell
Memory cell | Bit Line () | Output (bit) = Content | 
 |  | Active-high decoding logic | Active-low decoding logic
With n-MOS | 0 | 0 | 1
Empty | 1 | 1 | 0
Memory cell |  | Output (bit) = Content | 
 |  | Active-high decoding logic | Active-low decoding logic
With n-MOS | 0 | 0 | 1
Empty | 1 | 1 | 0

## Slide 25: ROM – Remarks and applications*
The one shown is called also mask-ROM
  Remember about the photolithographic masks employed in the semiconductor manufacturing process
  Each memory content corresponds to a different layout (of transistors), or, in other words, to a different integrated circuit
  Thus, to a different mask to realize that layout (or circuit)

## Slide 26: ROM – Remarks and applications*
Photolithographic masks have high costs
  Only for applications that require high volumes of ROM
Memory content cannot be modified
  The modification of just one bit (due to updates or bugs) means wasting the entire chip (and all other chips with the same content)
  Only for solid applications for which you are largely sure about the content of the memory

## Slide 27: PROM*
In the course of technological progress, mask-ROM has evolved into Programmable ROM (PROM)
  Still a ROM, Read-Only Memory
  But whose content is defined after the manufacture (of the integrated circuit)
    Not during the manufacture like the mask-ROM
  This allowed for a reduction in production costs because …
    For mask-ROMs: different memory content → different integrated circuit → different production line (masks, …)
    For PROM: always the same integrated circuit → the same production line

## Slide 28: PROM*
So, after production the PROM must be “written” to define its content
  This operation is called Programming
    From here the name
  Just one time
    OTP = One Time Programmable

## Slide 29: PROM*
So, after production the PROM must be “written” to define its content
  This operation is called Programming
    From here the name
  Just one time
    OTP = One Time Programmable
For this purpose, each memory cell contains a transistor + a fuse
  The fuse is an electronic component that …
    … by default, is a connection (a short circuit)
    … when subjected to a very strong current, it breaks down, breaking the connection (it becomes an open circuit)

## Slide 30: PROM – Architecture*
Memory cell

## Slide 31: PROM – Architecture*
Memory cell
  Transistor (n-MOS)

## Slide 32: PROM – Architecture*
Memory cell
  Transistor (n-MOS)
  Fuse

## Slide 33: PROM – Architecture*
Memory cell
  Transistor (n-MOS)
  Fuse
(default)

## Slide 34: PROM – Architecture*
Memory cell
  Transistor (n-MOS)
  Fuse
(default)
(after high current flow)

## Slide 35: PROM – Principle of operation*
Thus, programming means selecting which fuses to break (by injecting a high current)
  Programmed fuse = broken fuse = open circuit
  Unprogrammed fuse = default-state fuse = short circuit

## Slide 36: PROM – Principle of operation*
For this purpose, high voltage pulses (VPP = 10/30 V) must be applied to
  Gate terminal of n-MOS = Word Line
  Drain terminal of n-MOS = Bit Line
  n-MOS is in “high conduction” region = very high current
VPP
VPP
VPP
VPP

## Slide 37: PROM – Principle of operation*
By selecting (only) the corresponding Word Line and Bit Line, each memory cell can be programmed (or not) without the risk of accidentally programming cells that should do not
  A dedicated interface is required
After programming, the PROM works exactly like the mask-ROM
  Not programmed cell = cell with transistor → 0 on BL → 0/1 on output (Q)
  Programmed cell empty cell → 1 on BL → 1/0 on output (Q)

## Slide 38: PROM – Principle of operation*
Example
  Before programming

## Slide 39: PROM – Principle of operation*
Example
  After programming

## Slide 40: PROM – Principle of operation*
Example
  Reading cell (0,2)

## Slide 41: PROM – Remarks and applications*
Anti-fuses can be used instead of fuses
  Opposite of fuse
    Default (not programmed) = open circuit
    Programmed (with high current flow) = short circuit
Early PROMs had reliability problems
  Incompletely vaporized fuses
  Floating shrapnel inside the IC package
Target applications
  The same as mask-ROMs