## Slide 1: Electronics Systems (938II)
Lecture 3.3
Semiconductor Memories – EPROM and EEPROM

## Slide 2: Brief recall*
Evolution of Read-Only Memories (ROMs)
Mask-ROM

## Slide 3: Brief recall*
Evolution of Read-Only Memories (ROMs)
Mask-ROM
PROM

## Slide 4: Brief recall*
Evolution of Read-Only Memories (ROMs)
Mask-ROM
PROM
Programmed after manufacturing

## Slide 5: Brief recall*
Evolution of Read-Only Memories (ROMs)
Mask-ROM
PROM
Programmed after manufacturing
Programmed during manufacturing

## Slide 6: What after?*
Evolution of Read-Only Memories (ROMs)
Mask-ROM
PROM
Programmed after manufacturing
Programmed during manufacturing

## Slide 7: EPROM*
Evolution of Read-Only Memories (ROMs)
  After PROM: Erasable PROM (EPROM)
Mask-ROM
PROM
Programmed after manufacturing
Programmed during manufacturing

## Slide 8: EPROM*
Evolution of Read-Only Memories (ROMs)
  After PROM: Erasable PROM (EPROM)
Mask-ROM
PROM
Programmed after manufacturing
Programmed during manufacturing
EPROM
Programmed after manufacturing

## Slide 9: EPROM*
Evolution of Read-Only Memories (ROMs)
  After PROM: EPROM
Mask-ROM
PROM
EPROM
UV-EPROM
EEPROM
Programmed after manufacturing

## Slide 10: EPROM*
Evolution of Read-Only Memories (ROMs)
  After PROM: EPROM
Mask-ROM
PROM
EPROM
UV-EPROM
EEPROM
Erased by optical
process (UV rays)
Programmed after manufacturing

## Slide 11: EPROM*
Evolution of Read-Only Memories (ROMs)
  After PROM: EPROM
Mask-ROM
PROM
EPROM
UV-EPROM
EEPROM
Erased by electrical process
Erased by optical
process (UV rays)
Programmed after manufacturing

## Slide 12: EPROM*
Generally speaking
  It is a ROM
    Run-time working principle similar to the that of mask-ROM/PROM
  That can be programmed
  And erased
    So reprogrammed !!!

## Slide 13: EPROM – Underlying Technology*
It relies on particular MOS transistors

## Slide 14: EPROM – Underlying Technology*
It relies on particular MOS transistors
  FGMOS = Floating Gate MOS
    In practice, a MOS + one additional (floating) gate

## Slide 15: EPROM – Underlying Technology*
It relies on particular MOS transistors
  FGMOS
    In practice, a MOS + one additional (floating) gate
      Traditional MOS transistor
G = (control) Gate
S = Source
D = Drain

## Slide 16: EPROM – Underlying Technology*
It relies on particular MOS transistors
  FGMOS
    In practice, a MOS + one additional (floating) gate
      Traditional MOS transistor
        Metal
G
S
D

## Slide 17: EPROM – Underlying Technology*
It relies on particular MOS transistors
  FGMOS
    In practice, a MOS + one additional (floating) gate
      Traditional MOS transistor
        Metal
        Oxide
G
S
D

## Slide 18: EPROM – Underlying Technology*
It relies on particular MOS transistors
  FGMOS
    In practice, a MOS + one additional (floating) gate
      Traditional MOS transistor
        Metal
        Oxide
        Silicon
G
S
D

## Slide 19: EPROM – Underlying Technology*
It relies on particular MOS transistors
  FGMOS
    In practice, a MOS + one additional (floating) gate
      Traditional MOS transistor
        Metal
        Oxide
        Silicon
G
S
D

## Slide 20: EPROM – Underlying Technology*
It relies on particular MOS transistors
  FGMOS
    In practice, a MOS + one additional (floating) gate
G
S
D
Floating Gate

## Slide 21: EPROM – Underlying Technology*
It relies on particular MOS transistors
  FGMOS
    In practice, a MOS + one additional (floating) gate
      Floating gate = empty (default)
        It behaves like a “traditional” MOS
G
S
D
Floating Gate

## Slide 22: EPROM – Underlying Technology*
It relies on particular MOS transistors
  FGMOS
    In practice, a MOS + one additional (floating) gate
      Floating gate = full of electrons (programmed)
        It behaves like a “traditional” MOS
        But with a higher →
G
S
D
Floating Gate

## Slide 23: EPROM – Underlying Technology*
It relies on particular MOS transistors
  FGMOS
    In practice, a MOS + one additional (floating) gate
      Using a reading voltage () on the gate (), such that
G
S
D
Floating Gate

## Slide 24: EPROM – Underlying Technology*
It relies on particular MOS transistors
  FGMOS
    In practice, a MOS + one additional (floating) gate
      Using a reading voltage () on the gate (), such that
        Transistor = ON, if not programmed ()
        Short circuit: D = S
G
S
D
Floating Gate
ON

## Slide 25: EPROM – Underlying Technology*
It relies on particular MOS transistors
  FGMOS
    In practice, a MOS + one additional (floating) gate
      Using a reading voltage () on the gate (), such that
        Transistor = OFF, if programmed ()
        Open circuit: D disconnected from S
G
S
D
Floating Gate
ON
OFF

## Slide 26: EPROM – Underlying Technology*
Applying FGMOS to semiconductor memories architecture …
  FGMOS symbol
G
S
D

## Slide 27: EPROM – Underlying Technology*
Applying FGMOS to semiconductor memories architecture …
  FGMOS symbol
G
S
D

## Slide 28: EPROM – Underlying Technology*
Applying FGMOS to semiconductor memories architecture …
  FGMOS symbol
G
S
D

## Slide 29: EPROM – Underlying Technology*
Applying FGMOS to semiconductor memories architecture …
  Working principle
    FGMOS not programmed
    Reading with on
      FGMOS = ON
      FGMOS = short circuit → →
      (logic)

## Slide 30: EPROM – Underlying Technology*
Applying FGMOS to semiconductor memories architecture …
  Working principle
    FGMOS programmed
    Reading with on
      FGMOS = OFF
      FGMOS = open circuit → →
      (logic) from pull-up resistor (R)

## Slide 31: EPROM – Underlying Technology*
Applying FGMOS to semiconductor memories architecture …
  Why does this work?
  Because of …
    Time required for programming/erasing
    Data retention
    Endurance

## Slide 32: EPROM – Underlying Technology*
Applying FGMOS to semiconductor memories architecture …
  Why does this work?
  Because of …
    Time required for programming/erasing
      Programming = injection of electrons into the floating gate
      Erasing = removal of electrons from the floating gate
      Erasing + programming (cycle) takes a time in the order of minutes

## Slide 33: EPROM – Underlying Technology*
Applying FGMOS to semiconductor memories architecture …
  Why does this work?
  Because of …
    Data retention
      Permanence time of electrons in the floating gate (once injected) years
      Greater than duration of typical electronic application

## Slide 34: EPROM – Underlying Technology*
Applying FGMOS to semiconductor memories architecture …
  Why does this work?
  Because of …
    Endurance
      Number of cycles (erasing + programming) = endurance
      Endurance is limited
        Moving electrons through the oxide degrades it
      However, it is not low: typically, in the range

## Slide 35: EPROM – Underlying Technology*
Two different kinds of FGMOS
  Changing the way electrons are injected into (programming) and removed from (erasing) floating gate
    FAMOS = Floating-gate Avalanche-injection MOS
    FLOTOX = Floating-gate Tunnel-Oxide MOS

## Slide 36: FAMOS transistor*
Same layout and symbol as FGMOS
  It was the first FGMOS
G
S
D
G
S
D
Floating Gate

## Slide 37: FAMOS transistor*
Working principle
  Electrons injection (programming)
    Avalanche effect = very high current → Floating-gate Avalanche-injection MOS
      (programming voltage, )
G
S
D
G
S
D

## Slide 38: FAMOS transistor*
Working principle
  Electrons removal (erasing)
    Exposure to UV light
G
S
D
G
S
D

## Slide 39: UV-EPROM (or EPROM)*
It is based on FAMOS transistor
  In practice, it is a PROM with FAMOS transistor instead of MOS + fuse (or anti-fuse)
  Erasing procedure = exposure to UV light
    From here the name → UV-EPROM
    The chip is encapsulated in a window
    Erasing the whole chip (ROM content) at once
  Also called just EPROM
    It was the first type of EPROM

## Slide 40: UV-EPROM (or EPROM)*
Working principle
  Reading: the same as ROM/PROM
    If transistor programmed → OFF
    Otherwise (not programmed) → ON
  Erasing: exposure to UV light
  Programming – Example
    Programming cell (1,1)

## Slide 41: UV-EPROM (or EPROM)*
Working principle
  Reading: the same as ROM/PROM
    If transistor programmed → OFF
    Otherwise (not programmed) → ON
  Erasing: exposure to UV light
  Programming – Example
    Programming cell (1,1)

## Slide 42: UV-EPROM (or EPROM)*
Working principle
  Reading: the same as ROM/PROM
    If transistor programmed → OFF
    Otherwise (not programmed) → ON
  Erasing: exposure to UV light
  Programming – Example
    Programming cell (1,1)
      All other and !

## Slide 43: FLOTOX transistor*
Some differences w.r.t. FAMOS transistor
  Floating gate extends over Drain and is separated from it by a very thin oxide layer

## Slide 44: FLOTOX transistor*
Some differences w.r.t. FAMOS transistor
  Floating gate extends over Drain and is separated from it by a very thin oxide layer
G
S
D
Floating Gate
G
D
Floating Gate
FAMOS
FLOTOX

## Slide 45: FLOTOX transistor*
Some differences w.r.t. FAMOS transistor
  Also the symbol is different
G
S
D
Floating Gate
G
S
D

## Slide 46: FLOTOX transistor*
Working principle
  Electrons injection (programming)
    Tunnel effect (thanks to the very thin oxide layer) → Floating-gate Tunnel-Oxide MOS
      : not specified
G
S
D
G
S
D

## Slide 47: FLOTOX transistor*
Working principle
  Electrons removal (erasing)
    Tunnel effect (again)
      : not specified
G
G
S
D
G
S
D

## Slide 48: EEPROM (or E2PROM)*
It is based on FLOTOX transistor
  In practice, it is a PROM with FLOTOX transistor instead of MOS + fuse (or anti-fuse)
    Ideally !!!
  Erasing procedure = tunnel effect due to electrical quantities
    From here the name → EEPROM = Electrically Erasable PROM
      Or E2PROM
    Erasing only selected memory cells (FLOTOX transistors)

## Slide 49: EEPROM (or E2PROM)*
It is based on FLOTOX transistor
  In practice, it is a PROM with FLOTOX transistor instead of MOS + fuse (or anti-fuse)
    Ideally !!!
  Erasing procedure = tunnel effect due to electrical quantities
    From here the name → EEPROM = Electrically Erasable PROM
      Or E2PROM
    Erasing only selected memory cells (FLOTOX transistors)

## Slide 50: EEPROM (or E2PROM)*
Architecture (ideal)

## Slide 51: EEPROM (or E2PROM)*
Architecture (ideal)
  Programming cell (0,1)

## Slide 52: EEPROM (or E2PROM)*
Architecture (ideal)
  Programming cell (0,1)

## Slide 53: EEPROM (or E2PROM)*
Architecture (ideal)
  Programming cell (0,1)
  All other
    Otherwise the other cells in the same are programmed !

## Slide 54: EEPROM (or E2PROM)*
Architecture (ideal)
  Programming cell (0,1)
  All other
    Otherwise the other cells in the same are programmed !
  All other
    Otherwise the other cells in the same are programmed !

## Slide 55: EEPROM (or E2PROM)*
Architecture (ideal)
  Programming cell (0,1)
  All other
    Otherwise the other cells in the same are programmed !
  All other
    Otherwise the other cells in the same are programmed !
  But … ERASE DISTURB !!!

## Slide 56: EEPROM (or E2PROM)*
Architecture (ideal)
  Similarly, WRITE DISTURB !!!
  Erasing cell (1,2)
  All other
    Otherwise the other cells in the same are erased !
  All other
    Otherwise the other cells in the same are erased !

## Slide 57: EEPROM (or E2PROM)*
Architecture (real) – To solve the problems
  Memory cell
    2 transistors
      1x FLOTOX
      1x n-MOS (pass transistor)

## Slide 58: EEPROM (or E2PROM)
Architecture (real) – To solve the problems
  How should be driven
    Notes
      , , , and indicate, respectively, all other , , , and different from , , , and
      = high impedance
Operation |  |  |  |  |  |  |  | 
Program (,) |  |  |  |  |  |  |  | 
Erase (,) |  |  |  |  |  |  |  | 
Read (,) |  |  |  |  |  |  | -- | 
Operation |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  | -- | 
Just for the sake of completeness
  It won’t be part of the exam!!