## Slide 1: Electronics Systems (938II)
Lecture 3.5
Semiconductor Memories – SRAM

## Slide 2: Introduction to Random Access Memory (RAM)*
With the term RAM (Random Access Memory), typically we indicate memories that are:
  RWM (Read and Write Memory)
  Volatile
Note
  EPROM or EEPROM (or Flash memory) could be seen as a sort of RWM, but…
    … for those devices, ‘writing’ (= erasing + reprogramming) is disruptive
    In RAMs (or better, RWM) writing is not disruptive

## Slide 3: Introduction to Random Access Memory (RAM)*
RAM classification
  Static RAM (SRAM)
    The memory content is hold over the time, as long as the memory is powered
  Dynamic RAM (DRAM)
    Even if the memory is powered, the memory content needs to be refreshed over the time, otherwise it is lost

## Slide 4: Introduction to Random Access Memory (RAM)*
RAM classification
  Static RAM (SRAM)
    The memory content is hold over the time, as long as the memory is powered
  Dynamic RAM (DRAM)
    Even if the memory is powered, the memory content needs to be refreshed over the time, otherwise it is lost

## Slide 5: SRAM – Memory cell*
Bistable = two closed-loop inverters
A
B

## Slide 6: SRAM – Memory cell*
Bistable = two closed-loop inverters
  Two stable states
  Stable = the state is not changed (unless external stimuli)
A
B

## Slide 7: SRAM – Memory cell*
Bistable = two closed-loop inverters
  Two stable states
  Stable = the state is not changed (unless external stimuli)
    State 1
A
B
1
0
1
0

## Slide 8: SRAM – Memory cell*
Bistable = two closed-loop inverters
  Two stable states
  Stable = the state is not changed (unless external stimuli)
    State 1
    State 2
A
B
1
0
1
0
0
1
0
1

## Slide 9: SRAM – Memory cell*
Bistable = two closed-loop inverters
  Two stable states
  Stable = the state is not changed (unless external stimuli)
    State 1
    State 2
A
B
1
0
1
0
0
1
0
1

## Slide 10: SRAM – Memory cell*
Bistable = two closed-loop inverters
  Two stable states
  Stable = the state is not changed (unless external stimuli)
    State 1
    State 2
    State 3 ???
A
B
1
0
1
0
0
1
0
1

## Slide 11: SRAM – Memory cell*
Bistable = two closed-loop inverters
  Two stable states
  Stable = the state is not changed (unless external stimuli)
    State 1
    State 2
    State 3 ??? → No! Unstable!!!
A
B
1
0
1
0
0
1
0
1

## Slide 12: SRAM – Memory cell*
Bistable
  CMOS implementation
    State 1
    State 2
1
0
A
B
VCC

## Slide 13: SRAM – Memory cell*
Bistable
  CMOS implementation
    State 1
    State 2
0
1
A
B
VCC

## Slide 14: SRAM – Memory cell*
Bistable
  Symbol

## Slide 15: SRAM – Memory cell*
Architecture
  Bistable
  2x access transistors
  = Word Line
  = Bit Line for Write
  = Bit Line for Read

## Slide 16: SRAM – Memory cell*
Architecture
  Bistable
  2x access transistors
  Also called 6T (6-Transistors) SRAM cell
    Other architecture exist
    Example: 4-transistors (4T)

## Slide 17: SRAM – Memory cell*
Architecture
  Bistable
  2x access transistors
  Also called 6T (6-Transistors) SRAM cell
    Other architecture exist
    Example: 4-transistors (4T)
      Resistors instead of pull-up p-MOS in the bistable

## Slide 18: SRAM – Memory cell*
Architecture
  Bistable
  2x access transistors
  Also called 6T (6-Transistors) SRAM cell
    However, 6T is the most diffused
      Performance vs. costs
    If you are interested in other SRAM cell circuits:
      https://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=10134887

## Slide 19: SRAM – Architecture and working principle*
Example – 4x4
  D = input (write) data
  Q = output (read) data
  W = write command
    1 = write
    0 = read
Row
decoder
Column decoder

## Slide 20: SRAM – Architecture and working principle*
Example – 4x4
  Read
    Cell (0,1)
Row
decoder
Column decoder

## Slide 21: SRAM – Architecture and working principle*
Example – 4x4
  Read
    Cell (0,1)
    W = 0
Row
decoder
Column decoder

## Slide 22: SRAM – Architecture and working principle*
Example – 4x4
  Read
    Cell (0,1)
    W = 0
Row
decoder
Column decoder

## Slide 23: SRAM – Architecture and working principle*
Example – 4x4
  Read
    Cell (0,1)
    W = 0
    Column decoder
      Activating access transistors of
Row
decoder
Column decoder

## Slide 24: SRAM – Architecture and working principle*
Example – 4x4
  Read
    Cell (0,1)
    W = 0
    Column decoder
      Activating access transistors of
Row
decoder
Column decoder

## Slide 25: SRAM – Architecture and working principle*
Example – 4x4
  Write
    Cell (0,0)
Row
decoder
Column decoder

## Slide 26: SRAM – Architecture and working principle*
Example – 4x4
  Write
    Cell (0,0)
    W = 1
Row
decoder
Column decoder

## Slide 27: SRAM – Architecture and working principle*
Example – 4x4
  Write
    Cell (0,0)
    W = 1
Row
decoder
Column decoder

## Slide 28: SRAM – Architecture and working principle*
Example – 4x4
  Write
    Cell (0,0)
    W = 1
    Column decoder
      Activating access transistors of
Row
decoder
Column decoder

## Slide 29: SRAM – Architecture and working principle*
Example – 4x4
  Write
    Cell (0,0)
    W = 1
    Column decoder
      Activating access transistors of
Row
decoder
Column decoder