## Slide 1: Electronics Systems (938II)
Lecture 3.7
Semiconductor Memories – Computer memory

## Slide 2: Summary of semiconductor memories*
So far, we have seen several semiconductor memories, each with advantages and disadvantages over the others
  Register/DFF
  ROM/PROM/EPROM/EEPROM/Flash
  SRAM
  DRAM

## Slide 3: Summary of semiconductor memories*
Let’s compare them
Memory technology | Cost* (T) | Speed (Delay) | Other
DFF | 10T – 20T | Very high (10 ps) | Volatile
SRAM | 4T – 6T | High (1-10 ns) | Volatile
DRAM | ≈1T | Medium (100 ns) | Volatile
Flash | 1T | Slow (100 μs) | Non-volatile
* T = Transistors

## Slide 4: Summary of semiconductor memories*
All the analyzed memory technologies are used in modern computers/computing systems for different purposes
Let’s take a look at modern computer memories

## Slide 5: Computer memory*
Hierarchical organization
  Each level interacts only with the higher one (if any) and the lower one (if any)
CPU
Register
Cache
(L1, L2, L3)
Main Memory
(“RAM”)
Persistent Storage
(Solid State Disk, SSD)

## Slide 6: Computer memory*
Hierarchical organization
CPU
Register
Cache
(L1, L2, L3)
Main Memory
(“RAM”)
Persistent Storage
(Solid State Disk, SSD)
On-chip
Off-chip

## Slide 7: Computer memory*
Hierarchical organization
CPU
Register
Cache
(L1, L2, L3)
Main Memory
(“RAM”)
Persistent Storage
(Solid State Disk, SSD)
Capacity
Cost
Density
Speed
Latency

## Slide 8: Computer memory*
Hierarchical organization
CPU
Register
Cache
(L1, L2, L3)
Main Memory
(“RAM”)
Persistent Storage
(Solid State Disk, SSD)
Capacity
Cost
Density
Speed
Latency
Register

## Slide 9: Computer memory*
Hierarchical organization
CPU
Register
Cache
(L1, L2, L3)
Main Memory
(“RAM”)
Persistent Storage
(Solid State Disk, SSD)
Capacity
Cost
Density
Speed
Latency
Register
SRAM

## Slide 10: Computer memory*
Hierarchical organization
CPU
Register
Cache
(L1, L2, L3)
Main Memory
(“RAM”)
Persistent Storage
(Solid State Disk, SSD)
Capacity
Cost
Density
Speed
Latency
Register
SRAM
DRAM

## Slide 11: Computer memory*
Hierarchical organization
CPU
Register
Cache
(L1, L2, L3)
Main Memory
(“RAM”)
Persistent Storage
(Solid State Disk, SSD)
Capacity
Cost
Density
Speed
Latency
Register
SRAM
DRAM
Flash

## Slide 12: Computer memory*
Summary
Computer Memory | CMOS Memory technology | Capacity | Latency | Cost/GB | Position
CPU registers | Register | 1 Kb | Very low (10 ps) | $$$$ | On-chip
Cache | SRAM | 1 KB – 10 MB | Medium-low (1-10 ns) | 100 – 1000 $ | On-chip
Main Memory | DRAM | 1 GB – 10 GB | Medium (100 ns) | 4 – 5 $ | Off-chip
Storage/SSD | Flash | 100 GB – 1 TB | Very High (100 μs) | 0.1 S | Off-chip

## Slide 13: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim

## Slide 14: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  Often, RAM (Main Memory) and ROM are used in the HDL design flow as just model for simulation
  Otherwise, if they are used for memory implementation, they require special and dedicated steps in the design flow
    E.g., Memory Compiler automation tools

## Slide 15: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  RAM

## Slide 16: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  RAM
Ports
  Address
  Write/Read command
  Input data (D)
  Output data (Q)

## Slide 17: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  RAM
Ports
  Address
  Write/Read command
  Input data (D)
  Output data (Q)

## Slide 18: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  RAM
Ports
  Address
  Write/Read command
  Input data (D)
  Output data (Q)
Memory shape
  Assume data width = B
  Assume address bit = N → 2N cells
  Shape = 2N × B

## Slide 19: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  RAM
Ports
  Address
  Write/Read command
  Input data (D)
  Output data (Q)
Memory shape
  Assume data width = B
  Assume address bit = N → 2N cells
  Shape = 2N × B

## Slide 20: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  RAM
Ports
  Address
  Write/Read command
  Input data (D)
  Output data (Q)
Memory shape
  Assume data width = B
  Assume address bit = N → 2N cells
  Shape = 2N × B
  In this example
    B = 8 ← [7:0] d , [7:0] q
    N = 10 ← [9:0] addr

## Slide 21: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  RAM
Ports
  Address
  Write/Read command
  Input data (D)
  Output data (Q)
Memory shape
  Assume data width = B
  Assume address bit = N → 2N cells
  Shape = 2N × B
  In this example
    B = 8 ← [7:0] d , [7:0] q
    N = 10 ← [9:0] addr

## Slide 22: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  RAM
Packed/Unpacked arrays
  Packed dimension : before signal name (the one seen so far)
  Unpacked dimension : after signal name

## Slide 23: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  RAM
Packed/Unpacked arrays
  Packed dimension : before signal name (the one seen so far)
  Unpacked dimension : after signal name
  Both optional and both without limitations
    Multiple dimensions of both kinds can be specified
  If only packed dimension(s) → packed array
  If only unpacked dimension(s) → unpacked array
  If both → mixed packed/unpacked array

## Slide 24: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  RAM
Packed/Unpacked arrays
  Packed array
    Contiguous groups of bits
    Just a smart organization
    Examples:
      reg [7:0] a
      reg [2:0] [3:0] b

## Slide 25: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  RAM
Packed/Unpacked arrays
  Unpacked array
    Non-contiguous groups of bits
    Examples:
      wire a [3:0]
      reg b [8]

## Slide 26: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  RAM
Packed/Unpacked arrays
  In this example

## Slide 27: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  RAM
Packed/Unpacked arrays
  Multidimensional packed/unpacked arrays
    Access following the order of unpacked dimensions (left to right) then packed dimensions (left to right)
    Example:
      reg [3:0][7:0] foo [8][24];
      foo[7][23][3][7];
        Access in this order: [8] → [24] → [3:0] → [7:0]

## Slide 28: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  RAM
Write logic
Read logic

## Slide 29: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  RAM
Simulation example
…

## Slide 30: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  RAM
Simulation example
  Write some locations and check by
    Visual inspection of waveform
    Reading and displaying written value
…
…
…

## Slide 31: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  RAM
Simulation example
  Write some locations and check by
    Visual inspection of waveform
    Reading and displaying written value
…
…
…

## Slide 32: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  ROM
Similar to RAM but
  Without input data (D)
  Without write/Read command
  Only read logic

## Slide 33: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  ROM
Similar to RAM but
  Without input data (D)
  Without write/Read command
  Only read logic

## Slide 34: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  ROM
Similar to RAM but
  Without input data (D)
  Without write/Read command
  Only read logic
But how to “write” content? In other words, how to initialize content of the ROM?

## Slide 35: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  ROM
Similar to RAM but
  Without input data (D)
  Without write/Read command
  Only read logic
But how to “write” content? In other words, how to initialize content of the ROM?
  readmem command (+ initial block)

## Slide 36: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  ROM
Similar to RAM but
  Without input data (D)
  Without write/Read command
  Only read logic
But how to “write” content? In other words, how to initialize content of the ROM?
  readmem command (+ initial block)
    $readmemh/$readmemb(“file path”, <memory variable>)

## Slide 37: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  ROM
Similar to RAM but
  Without input data (D)
  Without write/Read command
  Only read logic
But how to “write” content? In other words, how to initialize content of the ROM?
  readmem command (+ initial block)
    $readmemh/$readmemb(“file path”, <memory variable>)
    $readmemh if digits in file are hexadecimal
    $readmemb if digits in file are binary

## Slide 38: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  ROM
File content
  Example (“ROM.hex”)

## Slide 39: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  ROM
File content
  Example (“ROM.hex”)
    Same bit width per line

## Slide 40: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  ROM
File content
  Example (“ROM.hex”)
    Same bit width per line
    Each line = one address

## Slide 41: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  ROM
ROM initialization inside an initial block
  This is not synthesizable
  This approach can be used only for modelling ROM
  Synthesizable-code approaches available, but omitted for simplicity

## Slide 42: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  ROM
Simulation example
  Read each address and display value to manually check against the content of initialization file

## Slide 43: Exercise with SystemVerilog
Implementation of RAM/ROM (model) and simulation with Modelsim
  You can find all the files about this exercise in the dedicated folder on the Team of the course
    File > Electronics Systems module > Crocetti > Exercises > 3.7
      ‘ram’ sub-folder, for RAM-related SV files
      ‘rom’ sub-folder, for ROM-related SV files
  Try to design and simulate on your own
    An example of ROM initialization file in ‘rom > ROM.hex’