## Slide 1: Electronics Systems (938II)
Lecture 4.1
Programmable Logic Devices – Principles and PAL

## Slide 2: Introduction*
PLD = Programmable Logic Device
  Programming HW, not SW!
  Configurable logic elements that can implement different circuits
    Configuration #1 → circuit/logic function #1
    Configuration #2 → circuit/logic function #2
    …
  Not different pieces of HW, but the same piece of HW used in different ways!

## Slide 3: Introduction*
PLD
  We have already seen some examples of programmable connections
    Fuses/anti-fuses
    MOS transistors
    …
  And how to program logic functions?

## Slide 4: Principles of programmable logic*
Any combinational logic function can be represented by a Boolean expression
  Operators
    → OR (gate)
    → AND (gate)
    → NOT (gate)
  Forms
    Sum-of-Products (SP)
    Product-of-Sums (PS)

## Slide 5: Principles of programmable logic
Any combinational logic function can be represented by a Boolean expression
  Operators
    → OR (gate)
    → AND (gate)
    → NOT (gate)
  Forms
    Sum-of-Products (SP) → AND gates feeding an OR gate
    Product-of-Sums (PS)

## Slide 6: Principles of programmable logic
Any combinational logic function can be represented by a Boolean expression
  Operators
    → OR (gate)
    → AND (gate)
    → NOT (gate)
  Forms
    Sum-of-Products (SP) → AND gates feeding an OR gate →
    Product-of-Sums (PS)

## Slide 7: Principles of programmable logic
Any combinational logic function can be represented by a Boolean expression
  Operators
    → OR (gate)
    → AND (gate)
    → NOT (gate)
  Forms
    Sum-of-Products (SP) → AND gates feeding an OR gate →
    Product-of-Sums (PS)

## Slide 8: Principles of programmable logic
Any combinational logic function can be represented by a Boolean expression
  Operators
    → OR (gate)
    → AND (gate)
    → NOT (gate)
  Forms
    Sum-of-Products (SP) → AND gates feeding an OR gate →
    Product-of-Sums (PS)

## Slide 9: Principles of programmable logic
Any combinational logic function can be represented by a Boolean expression
  Operators
    → OR (gate)
    → AND (gate)
    → NOT (gate)
  Forms
    Sum-of-Products (SP)
    Product-of-Sums (PS) → OR gates feeding an AND gate

## Slide 10: Principles of programmable logic
Any combinational logic function can be represented by a Boolean expression
  Operators
    → OR (gate)
    → AND (gate)
    → NOT (gate)
  Forms
    Sum-of-Products (SP)
    Product-of-Sums (PS) → OR gates feeding an AND gate →

## Slide 11: Principles of programmable logic
Any combinational logic function can be represented by a Boolean expression
  Operators
    → OR (gate)
    → AND (gate)
    → NOT (gate)
  Forms
    Sum-of-Products (SP)
    Product-of-Sums (PS) → OR gates feeding an AND gate →

## Slide 12: Principles of programmable logic
Any combinational logic function can be represented by a Boolean expression
  Operators
    → OR (gate)
    → AND (gate)
    → NOT (gate)
  Forms
    Sum-of-Products (SP)
    Product-of-Sums (PS) → OR gates feeding an AND gate →

## Slide 13: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS

## Slide 14: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case

## Slide 15: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #1
    AND gate/function

## Slide 16: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #1
    AND gate/function
    Truth table
    KM
a | b | y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 17: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #1
    AND gate/function
    Truth table
    KM
a | b | y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
 |  | b | 
 |  | 0 | 1
a | 0 | 0 | 0
 | 1 | 0 | 1

## Slide 18: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #1
    AND gate/function
    Truth table
    KM
a | b | y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
 |  | b | 
 |  | 0 | 1
a | 0 | 0 | 0
 | 1 | 0 | 1

## Slide 19: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #1
    AND gate/function
    Truth table
    KM
a | b | y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
 |  | b | 
 |  | 0 | 1
a | 0 | 0 | 0
 | 1 | 0 | 1

## Slide 20: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #1
    AND gate/function
    Truth table
    KM
a | b | y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
 |  | b | 
 |  | 0 | 1
a | 0 | 0 | 0
 | 1 | 0 | 1

## Slide 21: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #1
    AND gate/function
    Truth table
    KM
a | b | y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
 |  | b | 
 |  | 0 | 1
a | 0 | 0 | 0
 | 1 | 0 | 1

## Slide 22: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #1
    AND gate/function
    Truth table
    KM
a | b | y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
 |  | b | 
 |  | 0 | 1
a | 0 | 0 | 0
 | 1 | 0 | 1
How to
  Find all the largest group(s) of contiguous 1s
  For each group, select only the inputs whose value does not change
  Complement surviving inputs whose value is 0
  Multiply the surviving inputs → products
  Sum the products

## Slide 23: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #1
    AND gate/function
    Truth table
    KM
a | b | y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
 |  | b | 
 |  | 0 | 1
a | 0 | 0 | 0
 | 1 | 0 | 1
How to
  Find all the largest group(s) of contiguous 1s
  For each group, select only the inputs whose value does not change
  Complement surviving inputs whose value is 0
  Multiply the surviving inputs → products
  Sum the products

## Slide 24: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #1
    AND gate/function
    Truth table
    KM
a | b | y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
 |  | b | 
 |  | 0 | 1
a | 0 | 0 | 0
 | 1 | 0 | 1
How to
  Find all the largest group(s) of contiguous 1s
  For each group, select only the inputs whose value does not change
  Complement surviving inputs whose value is 0
  Multiply the surviving inputs → products
  Sum the products

## Slide 25: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #1
    AND gate/function
    Truth table
    KM
a | b | y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
 |  | b | 
 |  | 0 | 1
a | 0 | 0 | 0
 | 1 | 0 | 1
How to
  Find all the largest group(s) of contiguous 1s
  For each group, select only the inputs whose value does not change
  Complement surviving inputs whose value is 0
  Multiply the surviving inputs → products
  Sum the products

## Slide 26: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #1
    AND gate/function
    Truth table
    KM
a | b | y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
 |  | b | 
 |  | 0 | 1
a | 0 | 0 | 0
 | 1 | 0 | 1
How to
  Find all the largest group(s) of contiguous 1s
  For each group, select only the inputs whose value does not change
  Complement surviving inputs whose value is 0
  Multiply the surviving inputs → products
  Sum the products

## Slide 27: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #1
    AND gate/function
    Truth table
    KM
a | b | y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
 |  | b | 
 |  | 0 | 1
a | 0 | 0 | 0
 | 1 | 0 | 1
How to
  Find all the largest group(s) of contiguous 1s
  For each group, select only the inputs whose value does not change
  Complement surviving inputs whose value is 0
  Multiply the surviving inputs → products
  Sum the products

## Slide 28: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #1
    AND gate/function
    Truth table
    KM
a | b | y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
 |  | b | 
 |  | 0 | 1
a | 0 | 0 | 0
 | 1 | 0 | 1
Logic circuit
a
b
y

## Slide 29: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #2
    Truth table
    KM
a | b | y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
 |  | b | 
 |  | 0 | 1
a | 0 | 0 | 0
 | 1 | 1 | 1
How to
  Find all the largest group(s) of contiguous 1s
  For each group, select only the inputs whose value does not change
  Complement surviving inputs whose value is 0
  Multiply the surviving inputs → products
  Sum the products

## Slide 30: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #2
    Truth table
    KM
How to
  Find all the largest group(s) of contiguous 1s
  For each group, select only the inputs whose value does not change
  Complement surviving inputs whose value is 0
  Multiply the surviving inputs → products
  Sum the products
a | b | y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
 |  | b | 
 |  | 0 | 1
a | 0 | 0 | 0
 | 1 | 1 | 1

## Slide 31: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #2
    Truth table
    KM
How to
  Find all the largest group(s) of contiguous 1s
  For each group, select only the inputs whose value does not change
  Complement surviving inputs whose value is 0
  Multiply the surviving inputs → products
  Sum the products
a | b | y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
 |  | b | 
 |  | 0 | 1
a | 0 | 0 | 0
 | 1 | 1 | 1

## Slide 32: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #2
    Truth table
    KM
How to
  Find all the largest group(s) of contiguous 1s
  For each group, select only the inputs whose value does not change
  Complement surviving inputs whose value is 0
  Multiply the surviving inputs → products
  Sum the products
a | b | y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
 |  | b | 
 |  | 0 | 1
a | 0 | 0 | 0
 | 1 | 1 | 1

## Slide 33: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #2
    Truth table
    KM
How to
  Find all the largest group(s) of contiguous 1s
  For each group, select only the inputs whose value does not change
  Complement surviving inputs whose value is 0
  Multiply the surviving inputs → products
  Sum the products
a | b | y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
 |  | b | 
 |  | 0 | 1
a | 0 | 0 | 0
 | 1 | 1 | 1

## Slide 34: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #2
    Truth table
    KM
How to
  Find all the largest group(s) of contiguous 1s
  For each group, select only the inputs whose value does not change
  Complement surviving inputs whose value is 0
  Multiply the surviving inputs → products
  Sum the products
a | b | y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
 |  | b | 
 |  | 0 | 1
a | 0 | 0 | 0
 | 1 | 1 | 1

## Slide 35: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #2
    Truth table
    KM
Logic circuit
a
y
a | b | y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
 |  | b | 
 |  | 0 | 1
a | 0 | 0 | 0
 | 1 | 1 | 1

## Slide 36: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #3
    Truth table
    KM
a | b | y
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
 |  | b | 
 |  | 0 | 1
a | 0 | 1 | 1
 | 1 | 0 | 0
How to
  Find all the largest group(s) of contiguous 1s
  For each group, select only the inputs whose value does not change
  Complement surviving inputs whose value is 0
  Multiply the surviving inputs → products
  Sum the products

## Slide 37: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #3
    Truth table
    KM
How to
  Find all the largest group(s) of contiguous 1s
  For each group, select only the inputs whose value does not change
  Complement surviving inputs whose value is 0
  Multiply the surviving inputs → products
  Sum the products
a | b | y
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
 |  | b | 
 |  | 0 | 1
a | 0 | 1 | 1
 | 1 | 0 | 0

## Slide 38: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #3
    Truth table
    KM
How to
  Find all the largest group(s) of contiguous 1s
  For each group, select only the inputs whose value does not change
  Complement surviving inputs whose value is 0
  Multiply the surviving inputs → products
  Sum the products
a | b | y
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
 |  | b | 
 |  | 0 | 1
a | 0 | 1 | 1
 | 1 | 0 | 0

## Slide 39: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #3
    Truth table
    KM
How to
  Find all the largest group(s) of contiguous 1s
  For each group, select only the inputs whose value does not change
  Complement surviving inputs whose value is 0
  Multiply the surviving inputs → products
  Sum the products
a | b | y
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
 |  | b | 
 |  | 0 | 1
a | 0 | 1 | 1
 | 1 | 0 | 0

## Slide 40: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #3
    Truth table
    KM
How to
  Find all the largest group(s) of contiguous 1s
  For each group, select only the inputs whose value does not change
  Complement surviving inputs whose value is 0
  Multiply the surviving inputs → products
  Sum the products
a | b | y
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
 |  | b | 
 |  | 0 | 1
a | 0 | 1 | 1
 | 1 | 0 | 0

## Slide 41: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #3
    Truth table
    KM
How to
  Find all the largest group(s) of contiguous 1s
  For each group, select only the inputs whose value does not change
  Complement surviving inputs whose value is 0
  Multiply the surviving inputs → products
  Sum the products
a | b | y
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
 |  | b | 
 |  | 0 | 1
a | 0 | 1 | 1
 | 1 | 0 | 0

## Slide 42: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #3
    Truth table
    KM
Logic circuit
a
y
a | b | y
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
 |  | b | 
 |  | 0 | 1
a | 0 | 1 | 1
 | 1 | 0 | 0

## Slide 43: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #4
    Truth table
    KM
a | b | y
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
 |  | b | 
 |  | 0 | 1
a | 0 | 1 | 1
 | 1 | 0 | 1
How to
  Find all the largest group(s) of contiguous 1s
  For each group, select only the inputs whose value does not change
  Complement surviving inputs whose value is 0
  Multiply the surviving inputs → products
  Sum the products

## Slide 44: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #4
    Truth table
    KM
How to
  Find all the largest group(s) of contiguous 1s
  For each group, select only the inputs whose value does not change
  Complement surviving inputs whose value is 0
  Multiply the surviving inputs → products
  Sum the products
a | b | y
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
 |  | b | 
 |  | 0 | 1
a | 0 | 1 | 1
 | 1 | 0 | 1

## Slide 45: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #4
    Truth table
    KM
How to
  Find all the largest group(s) of contiguous 1s
  For each group, select only the inputs whose value does not change
  Complement surviving inputs whose value is 0
  Multiply the surviving inputs → products
  Sum the products
a | b | y
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
 |  | b | 
 |  | 0 | 1
a | 0 | 1 | 1
 | 1 | 0 | 1

## Slide 46: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #4
    Truth table
    KM
How to
  Find all the largest group(s) of contiguous 1s
  For each group, select only the inputs whose value does not change
  Complement surviving inputs whose value is 0
  Multiply the surviving inputs → products
  Sum the products
a | b | y
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
 |  | b | 
 |  | 0 | 1
a | 0 | 1 | 1
 | 1 | 0 | 1

## Slide 47: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #4
    Truth table
    KM
How to
  Find all the largest group(s) of contiguous 1s
  For each group, select only the inputs whose value does not change
  Complement surviving inputs whose value is 0
  Multiply the surviving inputs → products
  Sum the products
a | b | y
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
 |  | b | 
 |  | 0 | 1
a | 0 | 1 | 1
 | 1 | 0 | 1

## Slide 48: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #4
    Truth table
    KM
How to
  Find all the largest group(s) of contiguous 1s
  For each group, select only the inputs whose value does not change
  Complement surviving inputs whose value is 0
  Multiply the surviving inputs → products
  Sum the products
a | b | y
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
 |  | b | 
 |  | 0 | 1
a | 0 | 1 | 1
 | 1 | 0 | 1

## Slide 49: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #4
    Truth table
    KM
Logic circuit
a
y
a | b | y
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
 |  | b | 
 |  | 0 | 1
a | 0 | 1 | 1
 | 1 | 0 | 1
b

## Slide 50: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #5
    Truth table
    KM
 |  | bc |  |  | 
 |  | 00 | 01 | 11 | 10
a | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 0 | 1 | 0
a | b | c | y
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 51: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #5
    Truth table
    KM
How to
  Find all the largest group(s) of contiguous 1s
  For each group, select only the inputs whose value does not change
  Complement surviving inputs whose value is 0
  Multiply the surviving inputs → products
  Sum the products
 |  | bc |  |  | 
 |  | 00 | 01 | 11 | 10
a | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 0 | 1 | 0
a | b | c | y
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 52: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #5
    Truth table
    KM
How to
  Find all the largest group(s) of contiguous 1s
  For each group, select only the inputs whose value does not change
  Complement surviving inputs whose value is 0
  Multiply the surviving inputs → products
  Sum the products
 |  | bc |  |  | 
 |  | 00 | 01 | 11 | 10
a | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 0 | 1 | 0
a | b | c | y
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 53: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #5
    Truth table
    KM
How to
  Find all the largest group(s) of contiguous 1s
  For each group, select only the inputs whose value does not change
  Complement surviving inputs whose value is 0
  Multiply the surviving inputs → products
  Sum the products
 |  | bc |  |  | 
 |  | 00 | 01 | 11 | 10
a | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 0 | 1 | 0
a | b | c | y
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 54: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #5
    Truth table
    KM
How to
  Find all the largest group(s) of contiguous 1s
  For each group, select only the inputs whose value does not change
  Complement surviving inputs whose value is 0
  Multiply the surviving inputs → products
  Sum the products
 |  | bc |  |  | 
 |  | 00 | 01 | 11 | 10
a | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 0 | 1 | 0
a | b | c | y
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 55: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #5
    Truth table
    KM
How to
  Find all the largest group(s) of contiguous 1s
  For each group, select only the inputs whose value does not change
  Complement surviving inputs whose value is 0
  Multiply the surviving inputs → products
  Sum the products
 |  | bc |  |  | 
 |  | 00 | 01 | 11 | 10
a | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 0 | 1 | 0
a | b | c | y
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 56: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
  Example #5
    Truth table
    KM
Logic circuit
a
y
 |  | bc |  |  | 
 |  | 00 | 01 | 11 | 10
a | 0 | 0 | 1 | 1 | 0
 | 1 | 0 | 0 | 1 | 0
b
a | b | c | y
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1
c

## Slide 57: Principles of programmable logic
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
    Similar approach can be used for PS
    However, the goal is not to learn how to use Karnaugh maps, but …

## Slide 58: Principles of programmable logic*
Example(s)
  Karnaugh map (KM or K-map) = graphical method to express logic functions as SP or PS
    Showing SP case
    Similar approach can be used for PS
    However, the goal is not to learn how to use Karnaugh maps, but …
… demonstrating that
any logic function can be implemented as a network of AND and OR (and NOT) gates!

## Slide 59: PAL*
Earliest PLDs were called Programmable Array Logic (PAL)
  Programmable network of OR, AND, and NOT gates
    Pre-defined network
    Programmable connections among gates
  PROM to program (and re-program) connections

## Slide 60: PAL*
Architecture outline

## Slide 61: PAL*
Architecture outline

## Slide 62: PAL*
Architecture outline

## Slide 63: PAL*
Architecture outline

## Slide 64: PAL*
Architecture outline
  Do you see familiarity with previous examples?

## Slide 65: PAL*
Architecture outline
  Do you see familiarity with previous examples?
    Recalling example #5

## Slide 66: PAL*
Architecture outline
  Do you see familiarity with previous examples?
    Recalling example #5
= non-programmed node (open circuit)
= programmed node (short circuit)

## Slide 67: PAL*
Architecture outline
  Do you see familiarity with previous examples?
    Recalling example #5
= non-programmed node (open circuit)
= programmed node (short circuit)

## Slide 68: PAL*
Architecture outline
  AND plane

## Slide 69: PAL*
Architecture outline
AND plane 1
AND plane 2
AND plane 3

## Slide 70: PAL*
Architecture outline
  Do you see familiarity with previous examples?
AND plane 1
AND plane 2
AND plane 3

## Slide 71: PAL*
Architecture outline
  Do you see familiarity with previous examples?
    Recalling example #5
AND plane 1
AND plane 2
AND plane 3

## Slide 72: PAL*
Architecture outline
  Do you see familiarity with previous examples?
    Recalling example #5
AND plane 1
AND plane 2
AND plane 3

## Slide 73: PAL*
Architecture outline
  Do you see familiarity with previous examples?
    Recalling example #5
AND plane 1
AND plane 2
AND plane 3

## Slide 74: PAL*
Programmable connection(s)
  Connecting input to AND gate
  Determining the type of PAL/PLD
    OTP = One-Time Programmable
      Fuse/Anti-fuse
    Reprogrammable
      UV-EPROM style (FAMOS)
      Flash memory style (Flash transistor)
Input pin
to AND gate

## Slide 75: PAL*
Programmable connection(s)
  Connecting input to AND gate
  Determining the type of PAL/PLD
    OTP = One-Time Programmable
      Fuse/Anti-fuse
    Reprogrammable
      UV-EPROM style (FAMOS)
      Flash memory style (Flash transistor)
Input pin
to AND gate
Similar to memory (ROM):
Word Line = input pin
Bit Line = AND gate input

## Slide 76: PAL*
OTP PAL
  Fuse
to AND gate

## Slide 77: PAL*
OTP PAL
  Fuse
    Default (Fuse not vaporized)
      Input pin () connected to the AND gate
to AND gate

## Slide 78: PAL*
OTP PAL
  Fuse
    Default (Fuse not vaporized)
      Input pin () connected to the AND gate
    Fuse vaporized (after programming)
      Link to the input pin broken
      AND gate input connected only to the pull-up resistor (R)
        Always logic 1
        Not altering the AND gate functionality!!!
to AND gate

## Slide 79: PAL*
Reprogrammable PAL
  UV erasable (FAMOS)
to AND gate

## Slide 80: PAL*
Reprogrammable PAL
  UV erasable (FAMOS)
    Default (FAMOS not programmed)
      If input pin () = logic 1 () → transistor ON
        AND gate input = logic 0
to AND gate

## Slide 81: PAL*
Reprogrammable PAL
  UV erasable (FAMOS)
    Default (FAMOS not programmed)
      If input pin () = logic 1 () → transistor ON
        AND gate input = logic 0
      If input pin () = logic 1 () → transistor OFF
        AND gate input = logic 1
to AND gate

## Slide 82: PAL*
Reprogrammable PAL
  UV erasable (FAMOS)
    Default (FAMOS not programmed)
      If input pin () = logic 1 () → transistor ON
        AND gate input = logic 0
      If input pin () = logic 1 () → transistor OFF
        AND gate input = logic 1
      Attention! Inverting logic / active-low logic!!!
to AND gate

## Slide 83: PAL*
Reprogrammable PAL
  UV erasable (FAMOS)
    Default (FAMOS not programmed)
      If input pin () = logic 1 () → transistor ON
        AND gate input = logic 0
      If input pin () = logic 1 () → transistor OFF
        AND gate input = logic 1
      Attention! Inverting logic / active-low logic!!!
    FAMOS programmed ()
      Transistor always OFF
      AND gate input always logic 1 (through pull-up resistor to )
        Not altering AND gate functionality!!!
to AND gate

## Slide 84: Evolution of PAL*
Output polarity configuration: active-high / active-low
AND plane 1
AND plane 2
AND plane 3

## Slide 85: Evolution of PAL*
Output polarity configuration: active-high / active-low
AND plane 1
AND plane 2
AND plane 3

## Slide 86: Evolution of PAL*
Output polarity configuration: active-high / active-low
AND plane 1
AND plane 2
AND plane 3

## Slide 87: Evolution of PAL*
Output polarity configuration: active-high / active-low
AND plane 1
AND plane 2
AND plane 3

## Slide 88: Evolution of PAL*
Output polarity configuration: active-high / active-low
AND plane 1
AND plane 2
AND plane 3

## Slide 89: Evolution of PAL*
Registered output for sequential logic
AND plane 1
AND plane 2
AND plane 3

## Slide 90: Evolution of PAL*
Feedback path for FSM implementation
AND plane 1
AND plane 2
AND plane 3

## Slide 91: Evolution of PAL*
MUX to select between combinational or sequential output
AND plane 1
AND plane 2
AND plane 3

## Slide 92: Evolution of PAL*
PAL has evolved by enriching its functionality/flexibility
Evolution to more complex PLDs (CPLDs) to the latest and most powerful configurable device
  FPGA = Field-Programmable Gate Array
PAL
CPLD
FPGA

## Slide 93: PAL – Last notes*
How PALs were programmed
  Dedicated equipment
  Programming language
    PALASM (PAL Assembler)
    CUPL (Compiler for Universal Programmable Logic)
    ABEL (Advanced Boolean Expression Language)

## Slide 94: PAL – Last notes*
How PALs were programmed
  Dedicated equipment
  Programming language
    PALASM (PAL Assembler)
    CUPL (Compiler for Universal Programmable Logic)
    ABEL (Advanced Boolean Expression Language)

## Slide 95: PAL – Last notes*
How PALs were programmed
  Dedicated equipment
  Programming language
    PALASM (PAL Assembler)
    CUPL (Compiler for Universal Programmable Logic)
    ABEL (Advanced Boolean Expression Language)

## Slide 96: PAL – Last notes*
How PALs were programmed
  Dedicated equipment
  Programming language
    PALASM (PAL Assembler)
    CUPL (Compiler for Universal Programmable Logic)
    ABEL (Advanced Boolean Expression Language)
First examples of HDL