## Slide 1: Electronics Systems (938II)
Lecture 4.2
Programmable Logic Devices – FPGA overview

## Slide 2: Introduction to FPGA*
Latest and most advanced PLD
  FPGA = Field-Programmable Gate Array
PAL
CPLD
FPGA

## Slide 3: Introduction to FPGA*
FPGAs are similar to PALs
  Programmable device for implementing different logic functions at hardware level
  The same piece of hardware, but different configurations → different circuits
  Memory-like programming approach
    OTP
      Anti-fuses
    Reprogrammable
      SRAM-based

## Slide 4: Introduction to FPGA*
How FPGAs are programmed
  From computer through USB
    Dedicated software
    Each vendor use a different EDA software
  Using latest HDLs
    Verilog
    VHDL
    SystemVerilog

## Slide 5: Introduction to FPGA*
However, FPGAs show some differences from PALs
  Routing
  Logic function block

## Slide 6: Routing*
Programmable routing wires
  Segmented wires
Fixed routing wires
  Programmable nodes
  Non-segmented wires
PAL
FPGA
Logic blocks

## Slide 7: Routing*
Segmented routing in FPGAs
  Higher flexibility
  Higher wire delay
    Can have an even greater impact on circuit speed (propagation delay) than the logic block

## Slide 8: Routing*
Output of a logic block
Input of a logic block
Wire segments
Programmable connections
…
…
…
…

## Slide 9: Routing*

## Slide 10: Routing*
Wire segments → C
Programmable connections → R

## Slide 11: Routing*
Wire segments → C
Programmable connections → R

## Slide 12: Routing*

## Slide 13: Routing*
Propagation delay of routing (number of RC cells)2
Each RC cell introduces a delay

## Slide 14: Routing*
Segmented routing in FPGA includes
  Switching matrices
  Local and global routing wires

## Slide 15: Routing*
How programmable connections are realized?

## Slide 16: Routing*
How programmable connections are realized?
  Anti-fuse (OTP FPGA)
    Anti-fuse symbol

## Slide 17: Routing*
How programmable connections are realized?
  Anti-fuse (OTP FPGA)

## Slide 18: Routing*
How programmable connections are realized?
  Anti-fuse (OTP FPGA)
Default
(not programmed)
(open circuit)
Programmed
(short circuit)

## Slide 19: Anti-fuse (in brief)*
Programming = application of a very high voltage (between two metal plates)
Metal
Programmed
(short circuit)
Non-conducting material
Default
(not programmed)
(open circuit)
Metal

## Slide 20: Routing*
How programmable connections are realized?
  SRAM (Reprogrammable FPGA)

## Slide 21: Routing*
How programmable connections are realized?
  SRAM (Reprogrammable FPGA)

## Slide 22: Routing*
How programmable connections are realized?
  SRAM (Reprogrammable FPGA)
Not connected
(open circuit)
Connected
(short circuit)

## Slide 23: Logic function block*
Configurable
  Based on Look-Up Table (LUT)
Fixed
  AND planes + OR
PAL
FPGA

## Slide 24: Logic function block*
LUT programmable memory
  Each memory location contains one of the output values of the function
  The inputs of the function form the memory address
    Each combination of the inputs addresses a different memory cell, so a different output value
Let’s see an example

## Slide 25: Logic function block*
Example
  Logic function defined as it follows:
  It is enough programming the LUT so that for each combination of the inputs and the memory output is the one corresponding to the definition above

## Slide 26: Logic function block*
Rationale
  defined as it follows:
LUT
Decoding logic

## Slide 27: Logic function block*
Rationale
  defined as it follows:
LUT
Decoding logic

## Slide 28: Logic function block*
Rationale
  defined as it follows:
LUT
Decoding logic

## Slide 29: Logic function block*
Rationale
  defined as it follows:
LUT
Decoding logic

## Slide 30: Logic function block*
Rationale
  defined as it follows:
LUT
Decoding logic

## Slide 31: Logic function block*
How is a LUT made?
LUT
Decoding logic

## Slide 32: Logic function block*
LUT architecture outline

## Slide 33: Logic function block*
LUT architecture outline

## Slide 34: Logic function block*
LUT architecture outline

## Slide 35: Logic function block*
LUT architecture outline
  Example:

## Slide 36: Logic function block*
LUT architecture outline
  Example:

## Slide 37: Logic function block*
LUT architecture outline
  Example:

## Slide 38: Logic function block*
LUT architecture outline
  Example:

## Slide 39: Logic function block*
LUT architecture outline
  Example:

## Slide 40: Logic function block*
How are memory cells realized?

## Slide 41: Logic function block*
How are memory cells realized?
  Anti-fuse (OTP FPGA)

## Slide 42: Logic function block*
How are memory cells realized?
  Anti-fuse (OTP FPGA)
Default
(not programmed)
Programmed
(short circuit)

## Slide 43: Logic function block*
How are memory cells realized?
  SRAM (Reprogrammable FPGA)

## Slide 44: Logic function block*
How are memory cells realized?
  SRAM (Reprogrammable FPGA)

## Slide 45: Logic function block*
The one in this example can called 2–LUT
  2 inputs
Earliest FPGAs were equipped with 3–LUTs
Modern FPGAs are equipped with 6–LUTs

## Slide 46: Logic function block*
Architecture outline
Inputs
Clock

## Slide 47: Logic function block*
FPGA
PAL
Inputs
Clock
AND plane 1
AND plane 2
AND plane 3
Inputs
Clock

## Slide 48: CLB*
The logic function block also embeds other resources to improve flexibility and performance
  The overall block is called Configurable Logic Block (CLB)
  It assumes different names based on the FPGA vendor
    Altera/Intel
      ALM = Adaptive Logic Module
    Xilinx/AMD
      CLB = Configurable Logic Block
      Slice (in older FPGAs)
    Microsemi/Microchip
      LE = Logic Elements

## Slide 49: CLB – Example
ALM
  Altera/Intel
  Cyclone V FPGA

## Slide 50: Architecture outline*
Finally, we can see the overall architecture of an FPGA
  Organized in regions
I/O banks
Global routing
Region

## Slide 51: Architecture outline*
Finally, we can see the overall architecture of an FPGA

## Slide 52: Architecture outline*
Finally, we can see the overall architecture of an FPGA
  IOB : Input/Output Block
  RAM : RAM memory block
  DSP : Digital Signal Processor
  ____ : local routing
  ____ : global routing

## Slide 53: Architecture outline*
Latest FPGAs can embed also a processor
  Processor typically called HPS = Hard Processing Systems
    Usually ARM processor
  The overall device typically called FPGA SoC
    SoC = System-on-Chip
I/O banks reserved for HPS

## Slide 54: Anti-fuse vs. SRAM*
Can be re-programmed
Volatile programming
  Need to be re-programmed after power-on
Low resistance against disturbances
  Electromagnetic disturb may change a SRAM bit, modifying the configuration and the functionality
Possibility to test before the release
OTP (One-Time Programmable)
Permanent programming
  Do not need to be re-programmed after power-on
Robust against disturbances
  E.g.: radiations → suitable for space applications
It is not possible to test before the release
Anti-Fuse FPGA
SRAM FPGA

## Slide 55: Are FPGA really used in modern applications?*
Yes! For different reasons and/or a combination of them
  Flexibility
  Time-to-market
  Costs

## Slide 56: Are FPGA really used in modern applications?*
Yes! For different reasons and/or a combination of them
  Flexibility
  Time-to-market
  Costs
    Possibility to re-program (SRAM FPGA) without changing/substituting the HW
      Bug fixing
      System update

## Slide 57: Are FPGA really used in modern applications?*
Yes! For different reasons and/or a combination of them
  Flexibility
  Time-to-market
  Costs
    Shorter time from being conceived until being available for sale
      3–6 Months vs. 3–5 years (typical time-to-market for ICs)

## Slide 58: Are FPGA really used in modern applications?*
Yes! For different reasons and/or a combination of them
  Flexibility
  Time-to-market
  Costs
    Do you remember of the photolithographic process to produce ICs?
    The masks employed the process are strongly expansive
      US $ 1–10 Million !!!
    It is a non-recurring cost () that is split over the volume of production ()
      → lower the volume , higher the cost per unit

## Slide 59: FPGA vs. IC – Cost vs. Volume of production*
Assume
  = Non-recurring costs
  = Recurring costs per unit
  = Total cost per unit
  = number of units
It follows that
  =
  = +

## Slide 60: FPGA – Last notes
Main vendors – EDA and main devices
  Altera/Intel
    EDA : Quartus Prime
    Main FPGA families : Cyclone, Arria, Stratix
  Xilinx/AMD
    EDA : Vivado
    Main FPGA families : Spartan, Kintex, Artix, Virtex
  Microsemi/Microchip
    EDA : Libero SoC
    Main FPGA families : PolarFire, SmartFusion, RT (Radiation Tolerant)